1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start checklist -- (Default autostart takes 4m23s)
1. Battery Switch ... BATT (right hand forward)
2. Main AC Gen Switch ... AC GEN (right hand forward)
3. DC Gen Switch ... DC GEN (right hand forward)
4. AAP: COM1, COM2, WMMC1, WMMC2 buttons ... ON (Avionics Activation Panel, right hand)
5. Intercom Switch ... INT COM (right hand)
6. COM1, COM2, TCN/ILS, MSL Volume Knobs ... On, as desired (right hand)
7. Silence warning by pressing Master Warning light.
8. HUD CONT, HUD BRT, UFCP BRT knobs ... On, as desired (UFC)
9. Start engine:
  1. Fuel Pump Switch ... START PUMP (forward) (left hand forward)
  2. Engine Control Switch ... ENG CTRL (forward) (left hard forward)
  3. Start mode selector switch ... START (middle, default) (left hand next to throttle)
  4. Press Throttle Stop to Idle (Bottom Thumb Button press). Keep throttle at idle.
  5. Ground Start Button ... Press and hold for approx 4 seconds, engine will start.
  6. Monitor start on EPI1 MFD page.
10. ECS Mode Knob ... NORM (right hand)
11. SHARS Switch ... SHARS (left elbow)
  1. Monitor alignment on EFIS MFD page, takes 1 minute.
12. Emergency Hydraulic Pump Switch ... EMG HYD (left elbow)
13. AAP: INS button ... ON (Avionics Activation Panel, right hand)
  1. Wait until left MFD displays DST page and center MFD displays INS page.
14. On UFC, press DST 4 button, top row should say DST 00.
15. Open kneeboard to first page to see initial lat/long, altitude, and heading, or use F10 map.
16. Press Arrow button to left of second row and enter latitude (N/S). Press Arrow button again to save.
  - To set N or S, press Arrow button to right of second row.
Press Arrow button to left of third row and enter longitude (E/W). Press Arrow button again to save.
  - To set E or W, press Arrow button to right of third row.
Press Arrow button to right of fourth row and enter altitude as 5 digits with leading zeros. Press Arrow button again to save.
  - To set + or - (above or below sea level), press Arrow button to left of fourth row.
1. Perform FAST or GC alignment (full GC alignment may be needed for best accuracy with GPS guided weapons):
  1. FAST:
    1. INS Mode Knob ... FAST or NAV (NAV does FAST alignment and then automatically switches to NAV)
    2. While aligning, on center MFD, press THDG OSB and enter true heading.
    3. When REMAIN TIME reaches 00:00:00 and FAST is blinking on center MFD, alignment is complete.
    4. INS Mode Knob ... NAV (if it isn't there already).
  2. GC:
    1. INS Mode Knob ... GC
    2. Center MFD will show alignment progress, takes 4 minutes.
    3. When REMAIN TIME reaches 00:00:00 and GC is blinking on center MFD, alignment is complete.
    4. INS Mode Knob ... NAV
2. AAP: NAV ... ON (Avionics Activation Panel, right hand)
3. Click Oxygen Tube Connector and G-Suit Connector to hook up suit. Tubes should look like they have caps when connected. (left side of seat)
4. Open Oxygen Valve by scrolling up (knob moves left/CCW) until it stops. OXY BLINK will blink next to warning light panel. (left elbow)
5. Eject Seat Safe/Arm Handle ... ARMED (SAFE/ARMED lever by left knee)
6. Ejection Seat Firing Handle Safety Pin ... Remove (click, Remove Before Flight ribbon should disappear) (center seat between legs)
7. AAP: CMBT ... ON, activates AAP: RDR, SNLK, OESP, RWR, IFF, SAIU buttons (Avionics Activation Panel, right hand)
8. On UFC, press HNS button, then press Arrow button to left of second row to set INS+GPS.
9. Radio Mode Selector knob ... TR or TR+G (left elbow)
10. Brake switch ... NORM (left hand forward), releases parking brake

Proceed with preflight checklist on next page.