1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, Jettison

Takeoff
1. Rotate at 140 to 180 kts, 10 deg pitch, don't exceed about 13 degrees or risk tailstrike.
2. Flaps optional, may be used if heavy.
3. Gear and flaps up before 300 kts.

Landing
1. Flaps and gear down under 300 kts.
2. Trim for onspeed AOA.
3. Flare just before touchdown.
Wheel brakes are effective, or you can use the drag chute (Shift-T5 down to deploy, Shift-T5 up to cut).

Jettison
1. When external tanks are empty, fuel gauge will reset, showing full internal fuel (5100 lbs) and counting down from there.
2. Go to SMS MFD page, then JET OSB, select stations to jettison, press Red Button to jettison. May be limited by speed, or bank and pitch angles. If not working, try slowing down.