1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Radios

Radios
COM1	R&S M3AR	VHF / UHF	108.000 to 173.975 MHz / 225.000 to 399.975 MHz	AM only??
COM2	R&S M3AR	VHF / UHF	108.000 to 173.975 MHz / 225.000 to 399.975 MHz	AM only??	Also used for datalink (ch. 199 or 200)

- Despite the docs saying otherwise, both COM1 and COM2 can be tuned to any VHF or UHF freq.
- List of preset channels and frequencies is shown in the built-in kneeboard pages. The list is updated if you edit the preset freqs.

Using UFC (preset channels only)
1. Select preset channel for COM1 or COM2:
  1. Press RTN button to go to home screen.
  2. Press L4 or R4 arrow OSB next to COM1 or COM2 to go to the COM1 or COM2 settings page.
  3. Press L4 or R4 arrow OSB again next to the channel number, enter new desired channel in NNN format, press that arrow button again to enter.
  4. Press RTN button to go to home screen.
2. Radio settings on COM1/COM2 pages after pressing L4/R4 arrow OSBs:
  1. PLN, CMS, TRS ... Radio modulation mode. Only PLN (Plain) is implemented.
  2. RT, RT+G ... Receive/Transmit or Receive/Transmit+monitor Guard (not sure if implemented)
  3. NE-, NES ... Datalink off/on (used for COM2 on channel 199 or 200 only)
  4. EMG ... Emergency channels menu. L2 or L3 arrow OSBs toggle UHF/UHF- or VHF/VHF-. When "-" is shown, radio is tuned to UHF Guard (243.000) or VHF Guard (121.500).
  5. SQ+, SQ- ... Squelch on/off (PLN modulation mode only).
  6. SLAV, MAST ... Datalink mode (COM2 on channel 199 or 200 only)
  7. TDMA, PTP ... Unknown function (datalink modulation mode??) (COM2 on channel 199 or 200 only)

Using COMM panel (use preset channels, edit preset channels, use manual frequency tuning):
All use of the COMM panel:
1. Press Radio Control Handover button (small black button below LCD screen). A light above it on the screen should turn on.
  1. COMM panel is only active when Handover is active. As soon as Handover is activated, the COMM panel settings become your current COM1 settings, and the radio is tuned to that setting. As soon as Handover is deactivated, COM1 is tuned back to whatever is set on the UFC.
  2. When using Handover, COM2 remains set to whatever it was set to on the UFC (including datalink).
  3. You can have a preset channel selected, and a different manual frequency, and both of those can be different from what's set on the UFC for COM1, so you can switch between 3 different radio tunings with just a couple button presses.
Tune preset channel or manual frequency (Handover must be active):
Set Radio Mode Selector knob to TR or TR+G.
1. COMM panel has 2 modes: PRE (preset channel) or MAN (manual freq). PRE has one submode: ENT.
2. Top row of the display changes depending on what mode you're in:
  - PRE mode (default), display is "PNNN" (NNN is the channel):
    - Press 2 - and 3 + buttons to decrement/increment the selected preset channel.
    - Press 7 P button to enter a new preset channel in NNN format betwen 001 and 200). It is active as soon as you finish entering it, no need to press ENT.
      - NOTE If you press 8 C, it will use a different radio modulation (CMS, not implemented). Press ◀ MAN or ▶ ENT to cancel the "C" entry.
    - Press ◀ MAN to go to MAN mode, or ▶ ENT button to go to ENT submode.
  - ENT submode, display is "PNNN> f":
    - Press 3 + button to cycle showing the preset channel and band, or the frequency and channel.
    - Press 5 A button to cycle transmitter power (not sure if that's actually modeled)
    - Press 0 PRE to return to PRE mode.
  - MAN mode, display is "PNNN.NNN" (NNN.NNN is the frequency):
    - Press 7 P button to enter a new frequency in NNNNNN format. It is active as soon as you finish entering it, no need to press ENT.
    - Press 0 PRE button to go to PRE mode.
Edit preset channels (Handover must be active):
1. Set Radio Mode Selector knob to TR or TR+G.
2. Select a preset channel that you want to edit, following steps above in PRE mode.
3. Set Radio Mode Selector knob to SET (all the way clockwise). Display should now show the frequency associated with the selected channel.
4. Press ▶ ENT button or 7 P button, enter the new frequency in NNNNNN format. It is active as soon as you finish entering it, no need to press ENT again.
5. Set Radio Mode Selector knob to TR or TR+G.
6. If you edited the channel currently tuned on the UFC, you may need to change the UFC channel to something else and then back in order to pick up the new frequency.