1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Waypoints, Navigation

Waypoints
There are 60 total waypoints, also called DEST (destination) points:
Waypoint number	Use
00	Aircraft initial position for INS alignment
01-29	Regular waypoints for navigation
30-35 (RP1-RP6)	Route Points for CM-802AK/AKG cruise missile
36-39 (PP1-PP4)	Pre-Planned target points for LS-6/GB-6 bombs
40	Current SPI (Sensor Point of Interest aka designated target) coordinates
41-49	Markpoints
50-58	Airfields closest to last navigation waypoint (non-editable)
59	BINGO airfield (editable)

Navigate to waypoint
1. On UFC:
  1. Press RTN to return to home screen.
  2. Press R1 arrow OSB, enter waypoint number in NN format, then press R1 arrow OSB again.
  3. Press R2 arrow OSB to toggle AUTO or MAN:
    - AUTO mode ... Waypoint will increment to the next point automatically within 2 nmi.
    - MAN mode ... Waypoint will not increment automatically (useful if using waypoint as target area if you're coming back)

Create a new waypoint manually
1. On UFC, press DST button to open DST page on left MFD.
2. On left MFD, press STEP OSB to step through to an empty waypoint. Or on UFC, press arrow OSB next to waypoint number and enter a number, then press that arrow button again.
3. Enter the coordinates:
  1. Latitude is on 2nd row, press arrow button on left to enter numbers in DDMMSS, press arrow button on right to select N/S.
  2. Longitude is on 3rd row, press arrow button on left to enter numbers in DDDMMSS, press arrow button on right to select E/W.
  3. Altitude is on 4th row, press arrow button on right to enter numbers in nnnnn feet, press arrow button on left to select +/- (above or below sea level).

Create waypoints using F10 map and DTC (must be done on the ground before takeoff)
1. Remove DTC card.
2. Go to F10 map, add label points named "WPTn" for waypoints, "RPn" for route points (CM-802 cruise missiles), or "PPn" for pre-planned targets (LS-6/GB-6 bombs).
3. Use Ground Crew menu to update DTC.
4. Insert DTC and load ALL.
  - (may not be necessary to load ALL, maybe only NAV??)

Creating Markpoints
1. Press MRK button on UFC.
2. Press UFC L2 arrow button to toggle OFLY/DSG mode. Number is the waypoint that will be created.
  - If in OFLY mode, altitude of point will be your current altitude, can be edited with DST button on UFC.
  - If in DSG mode, point will be created at your currently designated target (SPI).
Press MRK button again to create markpoint.
  - To cancel, press RTN or wait several seconds.

TACAN -- WIP
IMPORTANT: TACAN will not work while datalink is in use. Disable datalink (set to NE- instead of NES) or tune COM2 radio to channel other than 199.
1. On any MFD, press Menu OSB, then TACAN OSB.
2. Set MODE to A/G for ground TACAN stations, or A/A for air TACAN stations (air refueling).
3. Set CHANNEL and BAND as needed.
4. Set COURSE if you want to fly a specific heading to the TACAN.
5. Set ALT and VAR for the TACAN station's altitude and local magnetic variation. Not sure if needed??
6. On HSD page on MFD, box the TCN OSB (R5 OSB) to display the TACAN info.