1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Countermeasures, ECM

Countermeasures
- Press Countermeasures hat forward or backward to dispense selected program.
- You can carry up to 36 chaff and 32 flares.
- There are 5 release programs available, see below for configuration.
- Each program can be chaff, flares, or both, and have sequences and bursts of different amounts and times.
- To select program:
  1. On left MFD, press CMBT OSB (B2 OSB).
  2. Countermeasures setup is shown in the middle section, left hand side and middle.
  3. Press PROGxx OSB (L5 OSB) to cycle through programs. (L4 OSB also cycles programs, based on CM type, but may not cycle through all programs.)
  4. Press L3 OSB to cycle AUTO or MAN (currently selected mode is what is shown next to the OSB). MAN recommended.

Countermeasures programming
- Program countermeasures in the Options > Special tab. This will be loaded into your plane on the DTC card.
- Recommended to set the following for PROG01 and PROG02:
  (SQ = Sequence Quantity, SI = Sequence Interval, BQ = Burst Quantity, BI = Burst Interval)
Program	CM type	Chaff SQ	Chaff SI	Chaff BQ	Chaff BI	Flare SQ	Flare SI	Flare BQ	Flare BI
PROG01	CH+FL	1	1	0.0	0.2	1	1	1	0.0
PROG02	CH+FL	4	1	1	0.0	4	1	1	0.0

- PROG01 will dispense 1x chaff and 1x flare for each CM hat press.
- PROG02 will dispense 1x chaff and 1x flare, 4 times, 1 second apart, for each CM hat press.
- For reference, here are the default programs:
Program	CM type	Chaff SQ	Chaff SI	Chaff BQ	Chaff BI	Flare SQ	Flare SI	Flare BQ	Flare BI
PROG01	CH	3	2	4	0.2	1	1	1	1.0
PROG02	CH	3	1	3	1.0	1	1	1	1.0
PROG03	FL	1	1	1	1.0	2	2	4	0.2
PROG04	FL	1	1	1	1.0	3	1	4	1.0
PROG05	CH+FL	3	0.5	4	0.2	3	0.5	4	0.2

Using the KG-600 POD (Self Protection Jammer)
1. Make sure SPJ button on AAP is ON.
2. On left MFD, press CMBT OSB (B2 OSB) to see countermeasures info.
3. Jammer setup is shown in the middle section, right hand side.
4. Press Countermeasures Hat up to activate jammer. Turns on after 15 second BIT.
5. TYPE1 is jamming when your aircraft is locked, TYPE2 is jamming when your aircraft is swept by search radar.
6. FWD/BWD/F+B controls direction of jamming.
7. When jammer is powered on (SPJ button on AAP is on, not just when actively jamming), it can determine approximate slant range of emitters and will show their actual distance on the HSD. When jammer is powered off or no jammer is equipped, HSD shows emitters by threat rings as normal.