1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - All

NOTE: 6 G limit when faster than Mach 0.85. Slow down to pull more Gs.
Corner speed: 370 to 390 kts

All
Master Arm ... ON
Master Mode ... A/A (Pinky Switch up)

PL-5EII IR missile with ACM mode -- PANIC MODE -- WVR quick engagement using ACM radar
WIP needs verification
1. Dish Hat up to enter DGFT Master Mode and automatically select PL-5 missiles.
2. Gray Reset Hat selects ACM radar mode:
  1. F: BS mode (boresight scan, 4 deg circle on HUD, range 10 nmi)
  2. B: VT mode (default) (vertical scan, 10 deg horiz x 50 deg vert, range 10 nmi)
  3. L: SA submode (unknown function??)
  4. R: HA submode (HUD area scan, range 10 nmi)
3. When you have lock, uncage with Rear Thumb Button.
4. When you have tone, fire with Red Button.
5. When finished, Dish Hat press to return to previous Master Mode.

Radar Modes -- TODO

ACM Modes -- TODO

SD-10 STT -- TODO

SD-10 TWS -- TODO

PL-5EII (IR guided) -- TODO

Gun modes -- TODO

PL-5EII - IR all aspect, AIM-9M equivalent
SD-10 - Active radar, export version of PL-12, AIM-120B/C equivalent (roughly between B and C)