1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - TPOD use, Laser Rockets, LGBs

Master Arm ... ON (B2)
Master Mode ... A/G (Pinky Switch down)

A/G weapons use "programs" (e.g. PROG01, PROG02, etc.) shown at the top of the weapon configuration grid on the SMS page. Cycle through programs with Lower Gray Button. Each program has a weapon associated with it, as well as configuration for that weapon, so you can set up all your weapons ahead of time and then cycle through the programs, or you can use one program and set it to use different weapons.

TPOD use (WMD7 pod)
1. Turn on TPOD with CLDP button on Avionics Activation Panel (right hand).
2. On center MFD, press OSBs: Menu, POD, WMD7, OFF. Takes 60 seconds to warm up.
3. When warmed up, press CAGE OSB to uncage.
4. Press Dish Hat down until SOI is in center MFD.
5. Controls:
  - Slew ... TDC stick
  - Lock ... TDC press
  - Unlock target, return to center/default position ... Gray Reset Hat press
  - Narrow/Wide FOV ... Gray Reset Hat forward/backward
  - Toggle CCD/IR mode ... Gray Reset Hat left
  - Toggle BHOT/WHOT (only in IR mode) ... Gray Reset Hat right
  - Zoom in/out ... Middle Finger Hat up/down
  - Gain (brightness) increase/decrease ... Middle Finger Hat left/right
1. SP mode (Snowplow) is fully manual slewing, stabilized to horizon and aircraft heading. SLAV mode (Slave) is defaulted to look at your target designated through another sensor (waypoint, ground radar, etc.).
2. Press CODE OSB to set laser code. (Laser code used by the weapon is shown in the SMS page.)
3. Laser designator can be in AUTO or MAN mode. AUTO will lase automatically, MAN requires you to use Laser Designator On/Off key (Pinky Button press) to manually toggle the laser.

BRM-1 laser guided rockets
1. Designate target with TPOD (see steps above).
2. Select and arm rockets on SMS page:
  1. MODE ... DIR (direct)
  2. FUZE ... EFUZE
  3. QTY and INTERV ... As desired (usually 1 and SNGL)
  4. BR ALT ... As desired (Prevents weapon release under altitude, set to 0000 for none)
3. When IN RANGE cue appears, fire with Red Button.
4. Max range depends on altitude, can be fired from further than IN RANGE cue if high up.

LGBs with TPOD -- GBU-12/16/10
1. Designate target with TPOD (see steps above).
2. Select and arm bombs on SMS page:
  - MODE ... AUTO
  - FUZE ... NOSE or N+T
  - QTY and INTERV ... As desired (usually 1 and SNGL)
  - BR ALT ... As desired (Prevents weapon release under altitude, set to 0000 for none)
1. Fly toward bomb fall line.
2. Time To Target appears in lower left of HUD (line starting with T). Only changes when 15 seconds away from drop.
3. Release cue is the dashed line extending up from your velocity vector. When 10 seconds from release, line starts becoming solid. Tone will sound when you enter the release window. Press and hold Red Button to drop. Tone will sound again when you are out of the release window.