1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - C-701T/IR Maverick-equivalents, LD-10 ARM

All
Master Arm ... ON (B2)
Master Mode ... A/G (Pinky Switch down)

C-701 Maverick-equivalents without TPOD
1. Arm and select missiles on SMS page.
2. On any MFD, press Menu OSB, then POD, then TVIR to get missile camera page.
3. Press OFF OSB, BIT will flash as it warms up (takes about 30 seconds), text will change to ON - IDLE.
4. Press ON OSB, text changes from IDLE to SEARCH. Missile is now active.
5. Put SOI in MFD with the missile camera page. Control missile camera with Gray Reset Hat:
  - F/B: Narrow/Wide FOV
  - R: Toggle WHOT/BHOT
  - P: Unlock target, reset to center or slave point
1. Set target size with OSB at bottom right (5 m, 15 m, 45 m, 135 m, 400 m).
2. Lock target with TDC press.
3. Fire with Red Button when within range (about 10 nmi).

LD-10 ARMs
1. Arm and select missiles on SMS page.
2. Press PWR OFF OSB to turn to PWR ON and start alignment.
  - Alignment takes 3 minutes; done when ALN TIMING box says 00:00.
Select missile mode:
  - ACT (Active): Missile goes to current designated target location (SPI) and automatically seeks radars in that area. (Not sure what radius it searches, might not be much.)
  - PAS (Passive): Missile chooses on its own which radar to attack when fired.
  - SP (Self-Protect): Missile attacks any emitter currently targeting you.
When in range (about 40 nmi), fire with Red Button.