201 - Ground - Cold Start

Cold Start -- WIP needs verification
1. Cockpit door ... Close (RCtrl-C or click door handle)
2. Right wall switches:
  1. Battery 1 and 2 ... ON (middle row forward)
  2. Intercom, VHF-1, VHF-2, DL, VHF-TLK switches ... ON (bottom row)
  - Note: SA-TFL switch has no effect in game.
  1. FUEL QTY switch ... ON (middle row)
  2. Fire Extinguisher switch ... OPER (up position) (black guarded switch, upper row)
  3. STANDBY SAI switch ... ON (bottom row)
  4. Ejection system power switches ... ON (red striped guarded switches) (bottom row)
  5. NAV switch ... ON (for PVI-800) (middle row)
  6. FWD and AFT FUEL PUMP switches ... ON (middle row)
  7. LEFT, RIGHT, and APU FUEL SHUTOFF switches ... ON (black guarded switches, middle row)
  8. LEFT and RIGHT EEG switches ... ON (black guarded switches, middle row)
2. ABRIS power switch ... ON (lower left of ABRIS screen), takes about 2 mins to boot up
3. K-041 switch ... ON (left console rear outboard)
4. Right rear wall switches:
  1. EKRAN HYD TRANS PWR switch ... AUTO BASE (down) (black guarded switch)
  2. INU switch ... INU
    - MASTER CAUTION light ... Press to reset (left upper instrument panel)
  1. L-130 switch ... ON
  2. UV-26 OPER switch ... OPER
2. Start APU:
  1. Engine selector switch ... APU (center position) (left console)
  2. Engine start switch ... START (left console)
  3. START button ... Press to start APU (left console)
  - APU takes about 20 seconds to start, RPM and status is shown on gauge at left elbow.
1. Rotor brake ... OFF (down) (black lever on left console near floor)
2. Collective ... Full down, flat pitch
3. Start left engine:
  1. Engine selector switch ... LH (left engine) (left console)
  2. START button ... Press to start left engine
  3. When left engine RPM is 20% or more (gauge on right instrument panel, needle 1): left engine fuel cutoff lever ... OPEN (red lever on left console)
  - Engine should spool up to idle around 65% RPM??, rotor RPM also around 65%??
1. Start right engine:
  1. Engine selector switch ... RH (right engine) (left console)
  2. START button ... Press to start right engine
  3. When right engine RPM is 20% or more (gauge on right instrument panel, needle 2): right engine fuel cutoff lever ... OPEN (red lever on left console)
  - Engine should spool up to idle around 65% RPM??, rotor RPM also around 65%??
1. APU SHUTOFF button ... Press to turn off APU (left console)
2. APU FUEL CUTOFF switch ... OFF (black guarded switch, right wall middle row)
3. When engine and rotor RPM is stable: Left and right throttles ... Auto (PgUp 2x) (yellow levers at left elbow on floor)
  - Rotor should stabilize around 95% RPM??
1. LH and RH AC SYS GEN switches ... ON (right wall middle row)
2. IFF switch ... ON (black guarded switch, right wall middle row)
3. SAI ... Uncage and center (right instrument panel)
4. PVI-800 (right console forward):
  1. NAV mode knob ... OPER
  2. DL/OFF switch ... DL
5. Engage BANK HOLD and PITCH HOLD autopilot modes, other modes as well if desired

Proceed with Preflight checklist on next page.