202 - Ground - Preflight, Performance Limits

Preflight (hot start or auto started)
1. To rearm, set SPU-9 Intercom knob to GROUND CREW (left console inboard).
2. Throttle ... Automatic setting detent, about halfway (Coll Twist Grip to idle stop)
3. PVI-800 WPT button ... OFF (right console, keypad under ABRIS MFD)
4. Autopilot heading hold ... OFF (keep roll and pitch on) (right console, or B4 or Trim Hat left)
5. Self ID knob for datalink ... Unique numbers for all helis on same d/l radio freq (right console)
  - If you have the same ID as another helicopter, you won't see them on your ABRIS display, but you can still send and receive targets from them. If two or more other helicopters have the same ID, you'll see them both on your ABRIS, but their icons will blink intermittently.
1. Datalink mode knob ... WINGM (right console) (allows you to send/receive to all planes in flight; COM only allows you to send data to wingmen, not receive it (Volk says COM only means you have a double circle instead of a single circle on other heli's displays??))
2. ABRIS ... NAV page (press OSB 5 until you're on the NAV page, then MAP OSB to get zoom buttons)
3. Lights ... As needed
  - Main cockpit lighting ... Left rear panel, above left shoulder
  - Panel/instrument, rotor tip, anti-collision, and formation lights ... Right wall switches, lower row rear
  - Navigation lights ... Overhead console, left side
1. HUD brightness knob ... As needed (under HUD)
2. Master Arm ... ON (center console under Shkval screen)
3. Weapon launch mode ... Manual (under Master Arm switch)
4. Cannon ammo type and fire rate switches ... As desired (switches on center console under stores panel)
5. Laser designator ... Armed (shift-Coll Trigger 1st stage to toggle) (left console forward of collective)
6. Dust protection ... As needed (Coll Index Finger Hat press to cycle off -> anti-ice -> dust protection) (overhead console)
7. Countermeasures system ... Both sides (upper right corner of canopy frame), see below
8. Radios ... As needed (R-800 on left console forward of collective, used for datalink; R-828 on right console rear, see other pages)
9. Set a navigation destination in ABRIS (optional, see below)

Performance limits
- Max descent speed:
  - Over 30 kph (translational lift): Unlimited
  - Under 30 kph (no translational lift): ~4 m/s
- Max speed: ~300 kph (depends on air pressure, may be limited either due to retreating blade stall or to rotor coning in different conditions)
- When at or near max speed, avoid sudden maneuvers, particularly pitching up and/or to the right.
- Engine Power Indicator gauge on right wall forward shows engine power for current atmospheric conditions (temperature and pressure). B=takeoff mode, H=max continuous, K=cruise