503 - A/G - Kh-25ML

Master Arm ... ON
Weapon launch mode ... Manual
Laser designator ... Armed
HMS ... ON (Coll Metal Switch 3 up)

Kh-25ML -- Semi-active laser guided missile -- WIP, needs verification
Using self-lasing:
1. Select Kh-25ML missiles (Gray Reset Hat left for outboard stations). This should make a launch circle appear on your HUD.
2. Stores panel under Shkval should say "ПC"; first number is how many missiles you have left, second number is cannon rounds x10.
3. If multiple launch aircraft, set Laser Code Selector knob (center console under brightness knobs) to unique numbers.
4. Lock target with Shkval as described on other page.
5. Max laser range is 15.0 km/8.1 nmi, missile max range may not be quite that far. Min range unknown, maybe 4 km??
6. Laser rangefinder/designator mode switch ... STDBY (left position) to set the laser to designator mode (black guarded switch under HSI compass)
7. When you are ready to fire, put the launch circle on the HUD over the target circle and press Coll Ministick press to begin lasing and allow missile to lock on the designator. Launch circle will flash while it is acquiring the laser, then go solid again when it's locked. A 40-second laser countdown will begin, shown on HUD.
8. Press and hold Red Button to fire. Aircraft will lurch to the side due to weight imbalance after launch.
  - The Kh-25ML has a backup inertial guidance system. After it begins its loft, if laser is turned off, the missile will try to fly to the last known laser point.
When finished, Laser rangefinder/designator mode switch ... MANUAL (right position) and close guard, and reset targeting system (Coll Index Finger Hat down). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.
Using buddy lasing (only between Ka-50s; other aircraft cannot buddy lase for Ka-50s):
1. On both aircraft, set Laser Code Selector knob (center console under brightness knobs) to the same number??
2. On buddy aircraft:
  1. Lock target with Shkval as described on other page.
  2. Laser rangefinder/designator mode switch ... STDBY (left position)
  3. When launching aircraft is ready, press Coll Ministick press to begin lasing. A 40-second laser countdown will begin, shown on HUD.
3. On launching aircraft:
  1. Select Kh-25ML missiles (Gray Reset Hat left for outboard stations). This should make a launch circle appear on your HUD.
  2. When the buddy aircraft begins lasing, the launch circle should start flashing and jump to the target location, indicating the missile is acquiring the laser.
  3. When the launch circle is solid again, fire with Red Button.