104 - Controls - Pilot - Collective Grip Alpha-L
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger -- HMD designate
- P1: --
- P2: Uncage Shkval, designate target (if using HMS, press and hold, look at target, then release; if not using HMS, sets Shkval on automatic left/right scan)
Flip-down Trigger
P: --
Trim hat -- Autopilot
- U: Autopilot Pitch hold (toggle) (alternate for B2)
- D: Autopilot Altitude hold (toggle) (alternate for B5)
- L: Autopilot Heading hold (toggle) (alternate for B4)
- R: Autopilot Bank hold (toggle) (alternate for B1)
- P: Hover hold on/off
- S-D: Descent Mode button (when in hover hold, press and hold to safely descend at 2-3 m/s)
Middle hat -- Shkval controls, (shifted) Targeting modes
- U: Narrow view (23x)
- D: Wide view (7x)
- R: Target frame size increase
- L: Target frame size decrease
- S-U??: Turn to target
- S-D??: A/A target
- S-L??: A/A head-on
- S-R??: Ground moving target
Ministick -- Shkval sensor
- Axes: Slew Shkval TV sensor
- P: Lock target (to unlock, press and hold while slewing in any direction)
Thumb hat -- Comms
- U: (SRS radio 1 PTT)
- D: (SRS radio 2 PTT)
- R: (SRS radio 3 PTT)
- S-U: Radio 1 PTT (opens comms menu for radio 1)
- S-D: Radio 2 PTT (opens comms menu for radio 2)
- P: (VoiceAttack PTT)
- S-P: (VoiceAttack center mouse cursor)
Index finger hat -- HMS, Targeting system reset, Engine dust/de-ice
- U: Helmet-Mounted Sight on/off (or NVG if fitted instead)
- D: Targeting system reset button (turns off Shkval and sets HUD to nav mode; if cannon is still selected, some cannon symbology will remain)
- P: Engine dust/de-icing switch cycle
Red Button -- Countermeasures
- P: Countermeasures Start dispensing (default program is 1 flare only)
- S-P: Countermeasures Stop dispensing
Black Button -- Autopilot flight director mode
P: Autopilot Flight Director mode (toggle) (turns off autopilot hold functions but leaves dampers on if roll and pitch channels are still on) (alternate for B3)
Scroll Wheel
- F: --
- B: --
- P1: --
- P2: --
Brake lever
- Axis: --
- P: --
Pinky button
P: --