301 - Flight - Preflight, Countermeasures, Navigation, Performance Limits

Before takeoff (hot start or auto started)
HOTAS:
Throttle ... Automatic setting detent, about halfway (Coll Twist Grip to idle stop)
Right console and wall:
1. PVI-800 WPT button ... OFF (right knee, keypad under ABRIS MFD)
2. Autopilot heading hold ... OFF (keep roll and pitch on) (right knee, or B4 or Coll Top Hat right)
3. Self ID knob for datalink ... 1 if you are flight lead, 2/3/4 if you are wingman
4. Datalink mode knob ... WINGM (allows you to send/receive to all planes in flight; COM only allows you to send data to wingmen, not receive it (Volk says COM only means you have a double circle instead of a single circle on other heli's displays??))
5. ABRIS ... NAV page (press OSB 5 until you're on the NAV page, then MAP OSB to get scale adjustments)
6. Lights ... As needed (rotor tip, anti-collision, and formation lights: right wall switches, lower row rear)
Center console:
1. HUD brightness knob ... As needed
2. Master Arm ... ON (center console under Shkval)
3. Weapon launch mode ... Manual (under Master Arm switch)
4. Cannon ammo type and fire rate switches ... As desired (switches on center console under stores panel)
Left console:
Laser designator ... Armed (Shift-Coll Red Button press)
Upper canopy frame:
1. Dust protection ... As needed (Shift-Coll Metal Switch 3 forward 2x to turn on)
2. Countermeasures system ... Both sides (upper right corner of canopy frame), see programming below
Other
1. Radios ... As needed (R-800 on left console forward of collective, R-828 on right console rear, see other pages)
2. Set a navigation destination in ABRIS (optional, see below)

UV-26 Countermeasures system
1. Left switch sets dispenser sides (left/both/right). Lights on display indicate selected side(s).
2. Right switch toggles between showing number of flares remaining, and flare program.
3. In flare program mode, display shows current program:
  - 1st number: Number of dispensing pulses
  - 2nd number: Number of flares per pulse
  - 3rd number: Number of seconds between pulses
1. Press NUM button (upper left) to increment 1st number (number in parens indicates actual number dispensed, e.g. 5=12 flares dispensed).
2. Press SEQ button (middle left) to increment 2nd number.
3. Press INT button (upper right) to increment 3rd number (number in parens indicates actual interval delay, e.g. 7=0.25 seconds).
4. Press RESET PROG button (middle right) to reset to default values (110).

Set a navigation destination in ABRIS
1. Press OSB 5 to cycle to NAV page. Press MAP OSB, then INFO. This centers your position on the map and enables a cursor.
2. Move the cursor on the map with the lower right knob on the ABRIS. Right-click the knob to toggle between moving left/right and up/down.
3. Press SCALE+ and SCALE- OSBs to zoom in and out, and recenter the map on the cursor.
4. When the cursor is over your destination, press INFO OSB again, then press TO OSB to set a direct course.
5. The DTA (Desired Track Angle), DST (Distance), and ETA is shown in the bottom center panel of the ABRIS. Your current track angle is shown at the top center.
6. Press SUSP OSB to cycle between showing route from start to destination, and destination to start.

Performance limits
- Max descent speed:
  - Over 30 kph (translational lift): Unlimited
  - Under 30 kph (no translational lift): ~4 m/s
- Max speed: ~300 kph (depends on air pressure, may be limited either due to retreating blade stall or to rotor coning in different conditions)
- When at or near max speed, avoid sudden maneuvers, particularly pitching up and to the right.