302 - Flight - Radios

Radio setup and tuning
COM1/CA(VHF-2)	R-800L1	VHF/UHF	VHF: 100.000 to 149.975 MHz UHF: 220.000 to 399.975 MHz	AM/FM	Also used for intra-flight datalink
COM2/VHF-1	R-828	LVHF	20.000 to 59.975 MHz	FM

All
On intercom panel (left console), set Radio Source Selector Knob to desired radio
  - "CA(VHF-2)" = R-800, "VHF-1" = R-828).
R-800 radio -- AM/FM, 100.000 to 149.975 MHz, 220.000 MHz to 399.975 MHz
1. On R-800 control panel (left console):
  1. Tune radio using dials. Dials have lag so don't click too quickly.
  - Verify the correct frequency in the SRS radio window.
  1. AM/FM switch ... As needed
  2. EM switch ... As needed (monitors guard when on, 121.500 or 243.000??)
  3. ADF switch ... OFF, unless using this radio for direction finding (TODO)
R-828 radio -- FM, 20.000 MHz to 59.975 MHz
1. On the R-828 control panel (right console rear):
  1. Turn red cross-shaped knob to desired channel.
  2. Press and hold the small "TUN" radio tuner button until the light turns on. If you let go too soon, it may not be tuned to the right frequency; in that case, turn the knob to a different freq, fully tune with the button, then change back to desired freq and re-tune.