401 - A/A - All

Using Vihkrs in A/A mode
1. Select Vihkrs (outboard weapon station, Gray Reset Hat left)
2. Lock target as normal with Shkval sensor.
3. Turn on the A/A mode targeting system button (Shift-Coll Metal Switch 1 back). This will make the Vihkrs trigger with a proximity fuse instead of direct impact.
4. If target is coming toward you quickly, turn on the A/A head on mode (Shift-Coll Metal Switch 2 forward). This will set the Vihkrs to trigger the proximity fuze sooner than it normally would.
5. Press Red Button to fire.

Using guns or rockets with a fixed gunsight
1. Set Autotracking switch to TS (Dish Hat press to toggle) (left console next to laser designator arming switch)
2. HUD will show pipper fixed in place. Shkval will show image boresighted to pipper.
3. Put pipper on target and fire with Trigger for gun or Red Button for rockets.
4. When finished, reset targeting system (Coll Metal Switch 3 back) and deselect cannon (Gray Reset Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.