502 - A/G - Rockets

Master Arm ... ON
Weapon launch mode ... Manual
Laser designator ... Armed
HMS ... ON (Coll Metal Switch 3 up)

Rockets
1. Select Rockets (Gray Reset Hat right for inboard stations, or Gray Reset Hat forward for all stations if carrying rockets on all stations).
2. Stores panel under Shkval should say "HP"; first number is how many rockets you have left, second number is cannon rounds x10.
3. Set burst length switch as desired (short = 1 rocket/pod, med = 5 rockets/pod, long=10 rockets/pod).
Using Shkval targeting system for automatic tracking
1. Lock target with Shkval as described on other page.
2. Once you are locked and in range, put the rocket reticle circle on the target. Fire with Red Button.
3. When finished, reset targeting system (Coll Metal Switch 3 back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.
Using boresight mode for manual aiming
1. Set Autotracking switch to TS (Dish Hat press to toggle) (left console next to laser designator arming switch)
2. HUD will show rocket pipper fixed in place. Shkval will show image boresighted to gun pipper.
3. Put pipper on target and fire with Red Button.
4. When finished, reset targeting system (Coll Metal Switch 3 back) and deselect cannon (Gray Reset Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.

Rocket types
- S-8 family - 80 mm, 20 rounds/pod, 1.3-4.0 km range
- S-8OFP2 - HE blast/frag warhead (due to DCS damage modeling, this is usually the best choice)
- S-8KOM - HEAT warhead
- S-8TsM - Smoke (often banned on servers due to lag issues)
- S-8OM - Illumination, launch at 7 km range, 15-20 deg up angle, starts burning at 17 sec after launch, burns for 35 sec
- S-13OF - 122 mm, 5 rounds/pod, HE blast/frag warhead, 1.6-3.0 km range