401 - A/A - All

9M342 Igla (SA-18 Grouse) on Strelets launchers -- IR guided A2A missile (Black Shark 3 only)
Short version:
1. Select A2A missile stations (Gray Reset Hat forward).
2. Press Red Button to begin cooldown: 5 seconds initial, then 55 seconds active time.
  - You can press RESET (Coll. Index Finger Hat back) to cancel the shot. If you haven't started into the second coolant bottle (>30 secs), you can press Red Button again to use the second one.
1. Press Ministick press to uncage and look for targets.
2. When locked, press Red Button again to fire.
Long version:
Select A2A missile stations (Gray Reset Hat forward).
  - A/A mode button should automatically light up (left console in front of collective handle).
  - Optionally enable A/A HO (Head On) for head-on engagements (Coll. Trim Hat right).
1. HUD will show:
  НАКОЛИ НИП	... CONNECT MSL PWR
  ИГЛА 1-4	... IGLA, and number of missiles remaining
  ЗПС or ППС	... rear aspect or frontal/head-on aspect, depending if A/A HO is enabled
2. Missile boresight is a small circle near the top center of the HUD.
3. When ready to engage, press Red Button to begin powering and cooling missile. Initial cooldown takes 5 seconds, then a countdown from 55 seconds appears on the HUD.
  - Each missile has 2 coolant bottles, used sequentially. Each bottle lasts 30 seconds (including any initial cooldown time). Once a bottle is in use, canceling it will lose the remaining coolant in that bottle.
  - If you cancel the shot (RESET button, Coll. Index Finger Hat back) before the first bottle is empty (>30 secs remaining in the countdown), you can use the second bottle by pressing Red Button again, which will do the 5-second initial cooldown, then count down 25 seconds of active time.
  - If you cancel the shot while the second bottle is in use, or if the coolant runs out, the missile is permanently disabled, and the system will move on to the next missile.
If in MAN weapons mode, press Target Lock button (Coll. Ministick press) to uncage missile seeker and allow it to search for targets. If in AUTO weapons mode, missile will uncage and begin seeking automatically.
  - Missile boresight circle on HUD will not initially change size, but seeker area is approximately a circle as big as the front window.
When a target is found, a buzzing tone sounds, the missile boresight circle gets bigger, and the currently tracked target is shown with a small + inside the circle.
  - Target cannot be changed manually; missile automatically tracks hottest target inside the circle??
1. Press Red Button again to fire.
2. Repeat from step 4 above for next missile.

Using Vihkrs in A/A mode
1. Select Vihkrs (outboard weapon station, Gray Reset Hat left)
2. Lock target as normal with Shkval sensor.
3. Turn on the A/A mode targeting system button (Coll Trim Hat left). This will make the Vihkrs trigger with a proximity fuse instead of direct impact.
4. If target is coming toward you quickly, turn on the A/A head on mode (Coll Trim Hat right). This will set the Vihkrs to trigger the proximity fuze sooner than it normally would.
5. Press Red Button to fire.

Using guns or rockets with a fixed gunsight
1. Set Autotracking switch to TS (Dish Hat press to toggle) (left console next to laser designator arming switch)
2. HUD will show pipper fixed in place. Shkval will show image boresighted to pipper.
3. Put pipper on target and fire with Trigger for gun or Red Button for rockets.
4. When finished, reset targeting system (Coll Index Finger Hat down) and deselect cannon (Gray Reset Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.