202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
1. All remaining CB switches ... ON except:
  1. DROP TANKS (unless carrying drop tanks)
  2. EMERG. RSBN
  3. CONNECTION IFF
2. Lights:
  1. Instrument/cockpit flood lighting and color ... Left wall behind throttle (L-39ZA) or left console forward (L-39C)
  2. Nav lights ... Right console middle
  3. Landing/Taxi lights ... Left canopy rail forward, below canopy lock lever
3. Radar Altimeter ... Set bug as desired
  - Reset Radio Altimeter warning tone by running altitude bug down to zero, then back up.
1. PITOT HEATING buttons ... As needed, both STAND-BY and MAIN (left console behind throttle)
2. Radios ... As needed (see other page for radio tuning)

Performance limits
- Fuel: 980 kg/2161 lbs internal
  - With 2x 150 L fuel tanks (116 kg/256 lbs each, 233 kg/513 lbs total) = 1212 kg/2673 lbs
  - With 2x 350 L fuel tanks (271 kg/598 lbs each, 542 kg/1196 lbs total) = 1523/3357 lbs
  - Fuel flow at full mil power at sea level/ISA is approx 1202 kg/2650 lbs per hr.
  - Endurance (sea level, ISA, mil power): 0h49m on internal fuel, 1h0m with 2x 150 L tanks, 1h16m with 2x 350 L tanks
- Speeds:
  - Max allowed speed: Mach 0.80, 900kph; airbrakes will extend automatically between Mach 0.76-0.80, which is just before the ailerons rip off
  - Tested max level speed at sea level in ISA conditions, no weapons:
    - L-39ZA: 719 kph / 388 kts / Mach 0.58 (same speed)
    - L-39C: 719 kph / 388 kts / Mach 0.58 (same speed)
  - Best climb speed: 350 kph
  - Landing gear down: 340 kph
  - Flaps (any position): 310 kph
  - Landing configuration stall speed: 145 kph
  - Elevator trim use: 700 kph
  - Wheel brakes: 190 kph
- Inverted flight: 20 secs, followed by at least 20 secs right-side-up
- Maximum crosswind for takeoff and landing: 10 m/s/19.4 kts
- Engine power and modes:
  - Max altitude with anti-ice: 8,000 m
  - Takeoff power:
    - Time: 20 min
    - RPM: 106.8%
    - EGT max up to 8,000 m: 685 C without anti-ice, 705 C with anti-ice
    - EGT max above 8,000 m: 715 C without anti-ice
    - Ceiling: 10,000 m
  - Max continuous
    - Time: Unlimited
    - RPM: 103.2%
    - EGT max: 650 C without anti-ice, 670 C with anti-ice
    - Ceiling: 12,000 m
  - On ground
    - Max EGT: 660 C; continuous: 625 C
  - Automatic EGT limiter:
    - RT-12 system is an automatic EGT (JPT) limiter. If on, and EGT reaches 700+/-15 deg C, fuel supply is automatically limited to prevent increasing temperature.
    - If EGT exceeds 730+/-15 deg C, JPT 730 deg C indicator comes on. If on ground, or if in the air then upon touchdown, engine will be shut down automatically.
    - RT-12 CB switch is on right console just forward of rear CB panel (default cold spawn is ON)