301 - Flight - Takeoff, Smoke System, Landing, Engine Restart

Takeoff
- Max takeoff weight: 5600 kg/12346 lbs
- Takeoff distance at max gross weight: 1280 m/4200 ft (assuming at sea level)
1. Taxi with differential braking, Rooskie brakes.
2. Flaps ... Takeoff (middle) position (T6 switch down)
3. Brakes will hold full mil power.
4. Unstick the nosewheel at 150 kph.
5. Rotate at 190-200 kph, up to 211 kph/114 kts at max gross.
6. Gear up before 340 kph.
7. Flaps up between 250-310 kph.
8. Climb at 350 kph.

Smoke (centerline and pods)
Turn on all weapon CBs (see Fence In steps on A/A or A/G pages), select inner pylons for centerline smoke, outer pylons for smoke pods. Toggle smoke with Trigger.

Landing
- Max landing weight: 4800 kg/10582 lbs
- Landing distance at max gross weight: 1070 m/3510 ft (assuming at sea level)
1. Under 340 kph, gear down.
2. Under 310 kph, flaps full down (shift-T6 switch down)
3. Approach speed is approx 230 kph, stall speed in landing configuration is about 145 kph.
4. Landing speed at max takeoff weight: 190 kph
5. At 8-10 m altitude, begin flaring and cut throttle, touchdown about 180 kph.
6. Rooskie brakes when all wheels are on the ground and under 190 kph.
7. After stopping, retract airbrake, set flaps to up, and reset trim (Trim Hat press).

Engine restart
If N1 is higher than 15%, windmilling restart:
  1. Throttle to STOP (all the way back and shift-Bottom Thumb Button to move back past rear detent).
  2. Maintain airspeed greater than 430 kph.
  3. Ensure N1 is still higher than 15%.
  4. Press ENGINE button for 2 seconds (left console forward under blue cover).
  5. After 3-6 seconds, move throttle to IDLE (Bottom Thumb Button press to move up past rear detent).
  6. Throttle up as RPM increases.
If N1 is lower than 15%, APU-assisted restart:
1. Throttle to STOP (all the way back and shift-Bottom Thumb Button to move back past rear detent).
2. Maintain airspeed between 300-350 kph.
3. Ensure N1 is still lower than 15%.
4. Press TURBO button for 2 seconds (left console forward under black cover).
5. When TURBINE STARTER caution light comes on (about 20 seconds), press ENGINE button for 2 seconds (left console forward under blue cover).
6. After 3-6 seconds, move throttle to IDLE (Bottom Thumb Button press to move up past rear detent).
7. Throttle up as RPM increases.