401 - A/A - A/A guns and missiles

Fence In
1. All weapon CB switches on center console top ... On
2. CANNON GS switch ... ARM (forward) (B2 button) (left wall outboard of throttle, partially hidden under canopy rail)
3. PYRO switch ... As needed (default is I) (left instrument panel)
4. EXPL CHARGE GS button ... Press to load gun using pyro charge (left instrument panel)
5. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
6. Trigger fires all weapons.

Cannon -- under-nose mounted GSh-23L, 23 mm, 150 rounds (L-39ZA only)
- IMPORTANT! For cannon to fire, speed must be over 400 kph/216 kts, AOA must be less than 6 deg (triangular AOA light to right of gunsight must be off), and G must be within -2 to +6. That means the cannon is not good for air to air!
- NOTE When firing, throttle is automatically cut to prevent engine flameout from gun gas ingestion. RPMs will continue to drop as long as gun is firing. Short bursts and sufficient speed recommended.
1. Charge cannon with Fence In steps above.
2. Gunsight can be set to GYRO or FIXED (default) with switch on the side of the base. In GYRO mode, gunsight will calculate lead for distance and wingspan:
  1. Set wingspan by rotating large knob on front of gunsight base.
  2. Set distance to match target with Middle Finger Hat up/down.
3. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
4. When firing conditions are met (speed, AOA, Gs), fire with Trigger.
  - There is no rounds counter, total firing time is about 2.5 secs.
- Wingspans:
  - MiG-29: 37 ft
  - F-16: 33 ft
  - Su-27: 48 ft
  - MiG-21: 24 ft
  - MiG-19: 30 ft
  - L-39: 31 ft
  - C-101: 35 ft

Gunpods -- PK-3 7.62 mm
- NOTE When firing, throttle is automatically cut to prevent engine flameout from gun gas ingestion. RPMs will continue to drop as long as gun is firing. Short bursts and sufficient speed recommended.
- PK-3 gunpods are not limited by speed, AOA, or Gs, unlike the internal cannon.
1. Charge guns with EXPL CHARGE GUNS switches on left instrument panel (OUTER and/or INNER as needed)
2. WEAPON CARRIER pushbuttons ... Select gunpod pylons (left button is outer, right button is inner)
  - Both pylons can be selected at once; if different weapons are loaded, only outer pylons will fire.
  - To deselect a pylon, press the small gray button below the white pushbutton.
1. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
2. Fire with Trigger.
  - There is no rounds counter, but total firing time is about 1m20s!
You can fire the GSh-23 cannon at the same time (provided firing parameters for the cannon are met) by turning on the PK3+GS switch (black guarded switch on left instrument panel)

Missiles -- R-60M limited all-aspect IR, R-3S rear-aspect IR
WEAPON CARRIER pushbuttons ... Select missile pylons (left button is outer, always outer pylons)
  - Both pylons can be selected at once; if different weapons are loaded, only outer pylons will fire.
  - To deselect a pylon, press the small gray button below the white pushbutton.
1. CONTROL SS HEATING and GLOWING switches ... ON (left wall outboard of throttle, hidden under canopy rail), and adjust tone volume as needed with knob
2. A/A switch ... PORT or STARB (B3 or B6 buttons) (left instrument panel)
3. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
4. Fire with Trigger.
5. Switch to next missile with: A/A switch ... STARB or PORT (B6 or B3 buttons) (left instrument panel)
- There is no ranging information, and the missile can lock well outside its effective range, so when in doubt, get closer.
- There is no cage/uncage.