503 - A/G - L-39C Bombs, Rockets

Fence In
1. All weapon CB switches on center console top ... On
2. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
3. Trigger fires all weapons.
4. Must be faster than 310 kph (170 kts) to fire weapons.

Rockets -- S-5KO, 16-round pods
1. Rockets Firing Mode selector 3-way switch ... As desired (center console, right side)
  1. 2RS -- 2 rockets fire with each press.
  2. 4RS -- 4 rockets fire with each press.
  3. AUT -- Fires continuously as long as trigger is held. Fires very quickly.
Quick presses of the trigger can fire fewer rockets in any of these modes.
1. Set gunsight depression (see tables on next page); 15 deg seems reasonable for short range attacks (while rocket motor is still burning).
2. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
3. Fire with Trigger.

Bombs
1. Missile/Bomb Release Selector Switch ... As desired (center console, right side)
  1. PORT (up) -- Drops left bomb only; must select STARBOARD to drop the other.
  2. STARBOARD (down) -- Drops both bombs simultaneously.
2. Set gunsight depression (see tables on other page)
3. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)
4. Fire with Trigger.