201 - Ground - Cold Start

Cold Start Checklist -- (Autostart takes 1m50s)
1. Canopy ... Close and lock (T7 up 2x)
2. Main Battery Switch ... ON (right console vertical panel)
3. Audio Warning Switch ... ON (right console forward, outboard)
4. Audio Warning Reset ... Press to silence warning (left instrument panel top)
5. If Special tab checkbox for ACLM alignment is checked??, INS Mode Selector knob ... NAV (right console middle)
6. If not checked, start INS alignment:
  1. INS Mode Selector knob ... STBY (right console middle)
  2. Open kneeboard and turn to the page with Initial Position, or get position from F10 map (DD MM.MM format, LAlt-Y to change format)
  3. INS Parameter Selector knob ... L/G (right console front)
  4. Press 1 on keypad for latitude field, then 2 for N or 8 for S, then enter latitude in DD MM.MM format, then INS Enter button.
  5. Press 4 on keypad for longitude field, then 4 for W or 6 for E, then enter longitude in DDD MM.MM format, then INS Enter button.
  6. INS Parameter Selector knob ... ALT (right console front)
  7. Enter altitude in feet (left display) or meters (right display):
    Feet:
    1. Press 1 to select left display, then 1 for positive altitude or 7 for negative, then enter altitude in NNNNN format, then INS Enter button.
    Meters:
    1. Press 3 to select left display, then 3 for positive altitude or 9 for negative, then enter altitude in NNNN format, then INS Enter button.
  8. INS Mode Selector knob ... ALN (right console middle)
  9. Validate Data Entry button ... Press (lights up after turning to ALN) (right console front)
  10. INS Operational Mode knob ... STS (right console middle)
  11. Displays now show alignment progress: Phase 1-5, seconds remaining for phase, total % remaining.
  12. When right display shows 000, alignment is complete.
  13. INS Operational Mode knob ... N (right console middle)
  14. INS Mode Selector knob ... NAV (right console middle)
7. Emergency Hydraulic Pump switch ... ON (right console front, outboard)
8. Start engine (right console rear):
  1. Fuel Cutoff Switch ... ON (right, and cover closed)
  2. Engine Fuel Left and Right Boost Pump switches ... ON (right)
  3. Starter Fuel Pump switch ... ON (right)
  4. Engine Start Switch Cover ... Open
  5. Ensure throttle is at full back position (press red Engine Shutdown Button on throttle track to set full back)
  6. Engine Start Switch ... Press, engine will start
  7. When engine RPM is at least 10%, move throttle forward past idle detent, then back to idle.
  8. Engine Start Switch Cover ... Closed
  9. When engine RPM is at least 60%, Starter Fuel Pump switch ... OFF (left)
9. HUD Power switch ... ON (middle position) (UFC, under overhang)
10. VTB Power switch ... ON (lower right of radar screen)
11. Radar Power Selector knob ... WARM UP (takes 3 mins) (left console outboard of throttle track)
12. Pitot Heat Switch ... ON and cover closed (right console forward, outboard)
13. Backup Gyro switch ... Energized (middle position) (right console middle, outboard)
14. Backup ADI ... Uncage and set to center (left instrument panel)
15. Wheel chocks ... Remove (ground crew menu, open canopy first)

Proceed with regular pre-flight checklist on next page.