202 - Ground - Preflight, Performance Limits

Preflight checklist (after hot or cold start)
Backup ADI power switch ... Energized (middle position) (right console middle, outboard)
  - Red fail flag on ADI should retract.
1. Parking Brake lever ... Down (right side of lower seatback)
2. FBW G-Limiter switch ... A/A or CHARGES as needed (doorbell-like warning will sound and CONF master caution light will illuminate if not correct) (B3 press to toggle)
  - Use CHARGES if you have a non-empty external fuel tank or A/G stores, A/A otherwise.
  - If you have an empty centerline tank, the caution panel will prompt you to switch to A/A mode.
1. Console and instrument lights ... As desired (right console)
2. BINGO ... As desired (default is 2800 kgs) (small numbers on right instrument panel above fuel panel, under fuel flow readout)
3. Radar Power Selector knob ... EMIT (left console outboard of throttle track) (Mode knob 4)
4. Radar Altimeter Power switch ... ON (UFC)
5. HUD Altimeter Selector switch ... RAD (adds radar altitude to HUD) (UFC)
6. HUD brightness ... As desired (left side of UFC)
7. Set up countermeasures systems (right console forward, aft of navigation panel):
  1. EW Mode Selector knob ... STBY or Square as desired, see Countermeasures page for details:
    1. STBY -- ECM is in standby, passive receive mode
    2. Square -- Automatic radar-priority jamming.
    3. PCM -- Automatic jammer-priority jamming (radar turns off while jamming).
    - According to the manual, DCS doesn't support targeted jamming or different jamming power levels, therefore jamming effectiveness is "similar" in both PCM and Square modes.
  1. BR (ECM), RWR, D2M (MLWS) switches ... ON (middle position) (D2M only works if enabled in mission editor)
  2. Decoy Release Mode switch ... S.A. or AUTO as desired (required to deploy chaff/flares)
  3. Decoy Release Program knob ... As desired (see Modes on next page)
  4. Radar IFF knob ... SECT or FULL as desired (FULL recommended)
2. Radios ... Set as needed, see Radios page for instructions.
3. RWR volume ... As desired (Marker Signal Volume knob, left console) (shift-E1 rotate)
4. Magic missile tone volume ... As desired (left console)
5. NWS ... Engage, blue light shows by landing gear indicator (Flip-down Trigger)
6. Ground Crew, Wheel Chocks ... Remove

Performance limits
- Fuel: 6978 lbs internal (3165 kg)
  - with 1300 L centerline drop tank (2183 lbs) = 9160 lbs (4155 kg)
  - with 2x 2000 L wing drop tanks (3484 lbs each, 6967 lbs total) = 13944 lbs (6325 kg)
- Landing Gear: 260 kts retracting, 230 kts extending
- Max speed: Approx 2.3 Mach at 45000 ft before wings ripped off