303 - Flight - Navigation Course, INS Updates, Markpoints

Route Desired (set a course to fly toward a waypoint)
On INS panel (right console forward)
1. Press PREP, then enter NN of waypoint to set course for.
2. Set knob to RD/TD (Route Desired/Time Desired).
3. Left numbers are Route in degrees true, right numbers are Time.
4. Press 1 or 7 for left numbers (route in degrees true), or 3 or 9 for right numbers (time), then enter value. Press INS to save, or EFF to cancel.
5. In NAV master mode, press RD button on PCA panel (above left knee) to enable route following symbology: small vertical lines ("| |") on the HUD and radar screen. Fly indicated heading to

INS update in NAV mode (for INS update while toss bombing, see A/G Weapons page for CCRP)
Using radar ranging
1. Gray Reset Hat press to set A/A mode to neutral.
2. Dish Hat down to set HUD to NAV mode.
3. Press OBL button on PCA panel (above left knee).
4. A diamond will appear on the HUD indicating where the radar is pointing.
5. When you are within 10 miles of the waypoint, a cross will appear on the HUD where the plane thinks the waypoint is.
6. Point the diamond at the correct location of the waypoint and press Rear Thumb Button ("Magic slave/AG designate/INS position update") to designate a new location for the waypoint.
7. On INS panel (right console forward), if the difference between current location and designated location is less than 15 nmi, the VAL button will turn on. Press the VAL button to accept the update, or REC button to reject the update.
Using direct overf‌light
1. Fly directly over the correct location for the current waypoint.
2. At the moment you fly over, press Forward Thumb Button ("Magic unlock/NAV update") to designate a new location for the waypoint.
  - NOTE: Forward Thumb Button for overflight updates, Rear Thumb Button for radar updates.
On PCN panel (right console forward), if the difference between current location and designated location is less than 15 nmi, the VAL button will turn on. Press the VAL button to accept the update, or REC button to reject the update.

Markpoints
- You have 3 markpoints available, numbered as waypoints 91, 92, and 93.
- Markpoints cannot be modified or deleted.
1. Press the MRQ button on the INS panel to show your current overflight location, then press VAL button to save that location as a markpoint (or REC button to reject the location??).
2. Second row of INS display will show M91, M92, M93 as markpoints are saved.
3. Navigate to markpoints as you would to waypoints numbered 91, 92, or 93.