401 - A/A - Radar Info

Radar Modes and general info:
- Radar starts in RWS. When you lock a target you'll either go to TWS or STT, depending on the radar mode: PSID or PID = TWS, PSIC or PIC = STT, toggle with Pinky Switch press.
- Press Dish Hat press ("Weapons SystemCMD Depress") to unlock a radar target.
- Use Mode dial on throttle to set radar power mode: Off (not mapped), Warm-up (3 mins), Stby, Emit.
- Change PRF modes with Pinky Switch up/down:
  - HFR (High) -- max range ~65 nmi, good look-down, but strong notch and rejects slow targets
  - ENT (Interleaved) -- max range ~45 nmi (will use HFR at ranges greater than 40 nmi), OK look-down, OK notch
  - BFR (Low) -- max range ~?, poor look-down, but no notch and can detect slow targets.
    - NOTE: CANNOT LOCK TARGETS IN THIS MODE (except when using BA2 horizontal ACM scan??)
- Middle Finger Hat controls bars (L/P/R = 4/2/1), elevation (U/D), scan azimuth/width (S-L/S-R).
- Set range by moving cursor to top or bottom (you can also set with dial on left console, not mapped)
- Radar search contacts:
  - ⋁ if they are heading toward you, ⋀ if they are heading away from you.
  - Closure rate in Mach on the right.
  - Wings on the top of the ⋁ or ⋀ mean they were picked up on bar 4 (top of scan altitude), line under the V means they were picked up on bar 1 (bottom of scan altitude), no wings or underline means they were picked up on bar 2 or 3 (middle of scan altitude).
  - Contacts may be doubled if they are detected on more than one bar sweep.
- Radar locked contact:
  - With locked contact, top row of radar screen shows target info: Mach, heading, closure (kts), altitude (ft x100).
  - Locked target itself shows target range nmi to left, closure (Mach) to right, aspect to lower right, arrow shows target flight direction.
  - In STT lock, target type (NCTR) is shown on bottom right of radar screen.
- Radar TDC cursor shows range to left, altitudes of scan volume to right.
- Press and hold Flip-down Trigger to IFF all targets on the screen. Friendly contacts have a solid diamond in the base of their V. Currently locked targets will show a line under their designator box on the HUD when the IFF interrogation has been done, and will have an "A" in the box if they are friendly.
- Elevation control type (switch on radar control panel):
  - S (SITE) -- HOTAS control directly moves the antenna elevation. (Default)
  - Z (ZBUT) -- HOTAS control sets the altitude of the center of the radar scan, and the antenna elevation is set to scan that altitude at the TDC position. Antenna elevation therefore changes as the TDC is moved.