501 - A/G - A/G Radar, Guns, Rockets

Fence In
- Master Arm ... ON (B2 button to toggle)
- Radar ... EMIT (Mode knob to 4)
- Gun arming switch ... ARM (B1 button to toggle)

A/G Radar -- WIP
- DEC mode (terrain avoidance)
  - DEC button to turn on (forward of throttle??), "A" button to turn off??
  - Max range 10 nmi??
  - Set safety clearance threshold with elevation up/down. -200 ft recommended. Terrain at the threshold altitude will be yellow, terrain above altitude will be red, below will be green.
  - DEC mode can be used with an A/A locked target as well, as SHB mode.
- VISU or VIS mode (ground mapping mode for navigation)
  - VIS button to turn on (under throttle??)
  - Up to 40 nmi range
  - adjust gain with knob under throttle
  - light color means stronger returns.
  - Can also be used to find ships

Mixing weapons
- Can have bombs, and rockets on inner wing pylon only. Rockets on outer wing pylon can be fitted but cannot be selected, so is not valid.
- Cannot mix A/G weapons with Super 530D missiles, only Magics.

Guns/Strafing
1. Press Gray Reset Hat press ("CNM Switch neutral").
2. On PPA (above right knee):
  1. 530D/Rockets/Guns Firing Mode Selector button ... TOT for continuous fire, PAR for 8 round burst (right side of PPA panel)
3. Gun Arm/Safe switch ... ARM (B1 press to toggle) (left console front vertical panel)
4. On PCA (above left knee):
  1. Gun Mode button ... Press so it shows "P" (left side of PCA panel)
  2. Select TAS and RS (Radar should be set to EMIT and Radar Altimeter should be ON).
  3. Select RAP (default) for rapid firing rate, LEN for slow firing rate.
5. Set HUD to CAS mode with Dish Hat up ("Weapons System CMD FWD").
6. Put pipper on target and press Trigger to fire.
  - In range when pipper starts to unwind. Ammo counters for left/right at bottom of HUD.
1. When done with cannon:
  1. Press Gun Mode button on PCA panel so the "P" goes away.
  2. Set HUD back to NAV mode with Dish Hat down ("Weapons System CMD AFT").

Rockets
1. Press Gray Reset Hat press ("CNM Switch neutral").
2. On PPA (above right knee):
  1. 530D/Rockets/Guns Firing Mode Selector button ... TOT for ripple fire, PAR for single rockets (right side of PPA panel)
3. On PCA (above left knee):
  1. Select RK3 for rockets.
  2. Select TAS and RS (Radar should be set to EMIT and Radar Altimeter should be ON).
  3. Select EXT or INT for outboard or inboard rocket pods, or both.
4. Set HUD to RK mode with Dish Hat up ("Weapons System CMD FWD").
5. Put pipper on target and press Trigger to fire.
  - In range when pipper starts to unwind. Ammo counters for left/right at bottom of HUD.
Set HUD back to NAV mode with Dish Hat down ("Weapons System CMD AFT").