503 - A/G - CCRP Bombs

Fence In
1. Master Arm ... ON (B2 button to toggle)
2. Radar ... EMIT (Mode knob to 4)
3. Gun arming switch ... ARM (B1 button to toggle)
4. Bomb fuzing, quantity, interval ... Set (PPA, above right knee)

Mixing weapons
- Can have bombs, and rockets on inner wing pylon only. Rockets on outer wing pylon can be fitted but cannot be selected, so is not valid.
- Cannot mix A/G weapons with Super 530D missiles, only Magics.

SAMP-250 note
As of 06/2022, SAMP-250 LD (slick) bombs don't have the right release profile and will always hit long. SAMP-250 HD (parachute retarded) works correctly.

CCRP bombs with visual target designation -- Mk 82 slicks, SAMP-250 LD, GBU-10/12/16
1. Press Gray Reset Hat press ("CNM Switch neutral").
2. On PPA (above right knee):
  1. Bomb Fuze Selector switch ... RET (delay fuze) or INST (instant fuze)
  2. Bomb Release Quantity Selector switch ... At least 1, or as desired. If 0, no bombs will drop.
  3. Bomb Release Interval Selector switch ... As desired, distance in meters
3. On PCA (above left knee):
  1. Select BL1 for Mk 82 low-drag slicks or EL1 for GBU.
  2. Select TAS and RS (Radar should be set to EMIT and Radar Altimeter should be ON).
4. Dish Hat up ("Weapons System CMD FWD") to set HUD to BL mode.
5. Fly to position the CCRP diamond on the target.
6. Press Rear Thumb Button ("Magic slave/AG designate/INS position update") to designate target.
  - NOTE The designator remains floating in the HUD, it does not stay locked on the designated target.
1. Follow the steering "wings" indicators on the sides of the CCRP diamond.
2. When you are 15 seconds from drop, horizontal release line will come up from the bottom of the HUD.
3. Hold Trigger until bombs drop when release cue reaches CCRP diamond.
  - If using GBUs, they will start guiding on their own when they see the laser.
Set HUD back to NAV mode with Dish Hat down ("Weapons System CMD AFT").

CCRP bombs with pre-planned target designation (e.g. toss bombing) -- Mk 82 slicks, SAMP-250, GBU-10/12/16
1. You must have a waypoint at a distinctive IP that you can use to update your INS just before the target, and you must have an offset on that waypoint to the actual target. To set up the offset, see steps on navigation and waypoints page.
2. Follow steps 1 through 4 above to set up bombs and avionics modes.
3. As you approach the IP waypoint you will need to do an INS update:
  1. When you are approaching the IP waypoint and it is the DEST waypoint, press PI ("Point Initial") button on PCA panel (above left knee).
  2. A diamond will appear on the HUD indicating where the radar is pointing.
  3. When you are within 10 miles of the IP waypoint, a cross will appear on the HUD where the plane thinks the waypoint is.
  4. Point the diamond at the correct location of the waypoint and press Rear Thumb Button ("Magic slave/AG designate/INS position update") to update the INS. You can press repeatedly to refine the location.
  5. Don't press the VAL button on the INS panel, and don't turn off the PI button on the PCA panel.
4. Continue flying toward and over the IP waypoint. The diamond should disappear from the HUD when you fly over it, and the HUD will show CCRP symbology.
5. 15 seconds from the target, a short horizontal bomb release line will appear at the bottom of the HUD and start moving upwards.
6. Pull up to about 15 to 20 degrees nose up and press and hold Trigger until release line meets velocity vector and all bombs drop.
7. Set HUD back to NAV mode with Dish Hat down ("Weapons System CMD AFT").