201 - Ground - Cold Start

Cold Start Checklist -- WIP
1. Canopy ... Close and lock
2. Flight control lock ... Remove and test for free stick movement (click on latch in front of stick base)
3. BATT switch ... ON (right console forward vertical panel)
4. Radios ... On (left console middle, behind throttle):
  1. Front radio function knob ... MAIN or BOTH
  2. Rear radio funciton knob ... T/R or T/R+G
5. Start engine:
  1. Ensure throttle is OFF (all the way back) (Shift-Bottom Thumb Button)
  2. Engine MASTER switch ... ON (left console forward inboard)
  3. JPT lLMTR switch ... ON (left console forward)
  4. Engine STARTER button ... Press and hold for 2 seconds (left console forward)
  5. When RPM is 10% or more: Throttle ... IDLE (bump throttle forward)
  6. Proceed with remaining items below; engine should eventually stabilize at about 42%.
6. GEN 1 and GEN 2 switches ... ON (right console forward vertical panel)
7. IN GPS power switch ... ON (right console forward outboard)
8. When AHRS/GPS is READY, begin alignment...
  - TODO
ANTI-SKID switch ... ON (left console middle inboard, next to throttle)
  - Begins self test; A/SKID warning light next to gunsight base should go out in 6-10 secs; Master Caution light should go out with it.
1. Flaps ... UP, then T/O (middle position)
2. Airbrake ... Retract (starts extended) (indicator on far left instrument panel, below clock)
3. IFF MASTER switch ... STBY, then NORM
  - IFF system should need to warm up in STBY mode first, but currently you can just turn it immediately to NORM after STBY. Not sure how long the warmup should take. IFF caution light will illuminate when in STBY mode.
1. Oxygen supply switch ... ON (green switch on left side of seat base)
2. Ejection seat safety pin ... Remove (front of seat base)
3. AHRS/GPS ... Load flight plan:
  1. TODO
4. If underwing pylon tanks equipped: FUEL TRANSFER switch ... PYL, otherwise leave set to TIP (left console middle inboard of throttle)
5. Parking brake ... OFF (left console front vertical panel, black and white striped handle above gear lever):
  1. Click on handle to turn it 45 degrees.
  2. Click and drag on shaft to push it forward, disengaging brake
6. Nosewheel steering ... ON (Flip-down Trigger)

Proceed with rest of preflight checklist on next page.