202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
1. INSTRUMENTS and CONSOLES lights ... As desired
2. External lights ... As desired
3. Radar Altimeter ... Set bug as desired??
4. ANTI-ICE PITOT and ENGINE switches ... As needed (right console middle outboard)
5. Radios ... As needed (see other page for radio tuning)
6. Navigation ... As needed (see other page for navigation systems)

Performance limits -- WIP needs verification
- Fuel:
  - Internal main tank:	626 kg (1380 lbs)
  - 2x 500 L cylindrical tip tanks:	802 kg (1768 lbs)
  - 2x 320 L elliptical tip tanks:	514 kg (1133 lbs)
  - 2x drop tanks:	530 kg (1168 lbs)
  - Internal + 500 L tip tanks:	1428 kg (3148 lbs)
  - Internal + 320 L tip tanks:	1140 kg (2513 lbs)
  - Internal + drop tanks:	1156 kg (2549 lbs)
  - Internal + 500 L tip tanks + drop tanks:	1958 kg (4317 lbs) (maximum possible fuel)
  - Internal + 320 L tip tanks + drop tanks:	1670 kg (3682 lbs)
- Engine limits:
  - Max continuous: 670 deg C, 95% RPM
  - Mil power, 20 mins: 756 deg C, 101.5% RPM
- Fuel flow (sea level, ISA):
  - Max continuous: approx 25 kg/min (3300 lb/hr)
  - Mil power: approx 34 kg/min (4500 lb/hr)
- Endurance:
  - Internal fuel:
    - Max continuous: 25m
    - Mil power: 18m
  - Internal fuel + 500 L tip tanks:
    - Max continuous: 57m
    - Mil power: 42m
  - Internal fuel + 350 L tip tanks:
    - Max continuous: 46m
    - Mil power: 34m
  - Internal fuel + 500 L tip tanks + drop tanks (maximum possible fuel:
    - Max continuous: 78m
    - Mil power: 58m
- Flaps:
  - Takeoff: 175 kts
  - Full: 150 kts
- Landing gear: 175 kts
- Landing light: 170 kts
- Max speed: 0.82 Mach or 500 kts, whichever is higher
- Max ground speed: 139 kts (tire limit)
- Taxi: 60 kts (canopy partially open)
- Max Gs: 8.0 (clean), 5.5 (full load)
- Negative G: 30 seconds max, followed by at least same amount of time at positive G
- Best climb speed: 275 kts (probably slower if heavier)
- Steepest climb speed: On-speed AOA (green circle in AOA meter)
- Tested max speed (sea level, ISA):
  - MB-339A clean (with pylons, no tip tanks):
    - Max continuous: 398 kts, Mach 0.64
    - Mil power: 480 kts, Mach 0.77
  - MB-339A with 500 L cylindrical tip tanks (500 L):
    - Max continuous: 397 kts, Mach 0.64
    - Mil power: 480 kts, Mach 0.74
  - 2x AIM-9M and DEFA 30 mm cannon
    - Mil power: 330 kts, Mach 0.495
    - MPR power: 343 kts, Mach 0.52