501a - A/G - Gun pods, Rockets, Bombs

Fence In
1. On gunsight base:
  1. PWR switch ... L1 (L1 is primary lamp bulb, L2 is backup bulb)
  2. DEPRESSION MILS ... 0 deg?? (default) is waterline, otherwise as needed, see below
2. Gunsight mode knob (on throttle handle):
  - MODE 1 – Air-to-ground firing, without roll control.
  - MODE 2 – Air-to-ground firing, with roll control.
  - MODE 3 – Air-to-air firing, 500 m range.
  - MODE 4 – Air-to-air firing, 300 m range.
  - According to the manual: "The gyro computing sight installed in the MB-339A aircraft automatically sets in the lead angle correction and fully corrects for velocity jump, gravity drop, etc., at two range values (300 to 500 m), with attack airspeeds between 330 and 350 KTAS, 290 KTAS target speed, 10000 ft flight altitude, 20° angle off and pursuit curve flown at 2,5 g (66° bank), aircraft mass of 4090 kg (9000 lb). Residual errors for non-standard attack conditions are very small."
MASTER ARMT switch ... ON (lower left instrument panel)
  - IMPORTANT: If MASTER ARMT switch is turned ON with weight-on-wheels (on ground), it will need to be turned OFF and then back ON once airborne.
If in rear seat, ensure FIRE switch is ON (default position, red guarded switch on armament control panel) to allow front-seat to fire weapons.

Gun pods -- 2x M2 .50 cal MGs (350 rounds/gun) or 2x DEFA 30 mm cannon (120 rounds/gun)
1. On Store Selection Panel (lower left instrument panel):
  1. Select gun pod stations (lights show selected stations)
2. Gunsight depression ... 10 deg??
3. Press Trigger to fire.

Rockets
1. On Store Selection Panel (lower left instrument panel):
  1. Select rocket pod stations (lights show selected stations)
  2. SEQUENCE switch ... RPL or SGL as needed:
    - RPL -- Rockets are ripple-fired continuously from all selected stations (currently fires all rockets with a single press of the pickle, even if you let go of the button, it keeps firing)
      - Salvo timing is set in the Mission Editor.
    - SGL -- Rockets are fired singly, one per pickle-press from each selected station
1. Set gunsight depression (see tables on next page); 35 deg is a good default for steep dives or close range attacks (rocket motor still burning) (Middle Finger Hat up/down for tens, left/right for units)
2. Press Red Button to fire.

Bombs
1. On Store Selection Panel (lower left instrument panel):
  1. Select bomb stations (lights show selected stations)
  2. BOMB FUZE switch ... NOSE/TAIL or TAIL as needed
  3. SEQUENCE switch does nothing??
  4. No ripple interval settings??
2. Set gunsight depression (see tables on next page) (Middle Finger Hat up/down for tens, left/right for units)
3. Pickle with Red Button.