201 - Ground - Cold Start
(autostart is as fast or faster than manual startup)
Cold Start -- WIP
1. Collective ... Full down
2. (default) Throttle twist grip ... MIN (full left) (right-click and drag on collective handle grip)
Circuit breakers and electric power
1. All circuit breakers on rear walls left and right of pilot's seat ... ON (use gang bars)
2. Left and Right Batteries ... ON (right console, DC POWER panel)
3. POWER FROM BATT switch ... ON (right console, DC POWER panel, green guarded switch)
4. DC Voltmeter knob ... BATT (right console, DC POWER panel)
5. PO-750A switch ... ON (right console, AC POWER panel, green guarded switch)
Prepare for engine start
1. Cockpit door ... Close and seal (Pneumatic Sealing Valve wheel on left wall)
2. Rotor Brake lever ... Down (off) (handle on floor to right of pilot seat)
3. Fire Protection Power ... ON (left wall forward)
4. Fire Extinguisher ... ON (left wall forward)
5. Fuel Tank Valves ... Open (left wall)
6. Engine Fire Cut-off Valves ... Open (left rear floor)
7. Separator Valve ... Open (left wall)
8. Fuel Pumps ... ON (left wall)
9. If using external fuel tanks: External Fuel Tanks switch ... ON (left wall)
Start APU
1. APU selector switch ... Start (down) (left wall)
2. APU start button ... Press for 2-3 seconds, start stopwatch on dashboard
3. Monitor: EGT max 880 deg C, DC voltage not less than 18V, Automatic Start On light off within 30 secs
4. Reset stopwatch
Start engines
1. Strobe light ... ON (left wall)
2. Start downwind engine first. For each engine:
  1. Engine Start Mode switch ... Start (down) (left wall)
  2. START button ... Press for 2-3 seconds.
  3. Engine Stop Lever ... Down (left of pilot's seat)
  4. Start stopwatch.
  5. Monitor: Automatic Start Enabled and Starter Running lights lit, engine and rotor RPM increasing, Starter Running light goes out when turbocharger?? speed is 60-65%, Automatic Start Enabled light goes out within 33 seconds.
  6. Repeat for other engine.
3. Allow both engines to idle for at least 60 seconds to warm up.
4. Dust Protection switch ... ON (left wall front, green guarded switch)
5. When engine oil temp > +30 deg C and gearbox temp > -15 deg C (gauges on right forward panel): Collective grip throttle ... Max (full right)
6. When main rotor RPM is 95% +/-2%: Generators ... ON (right console)
7. PO-750A switch ... OFF (right console, guarded switch)
8. 115V and 36V transformer switches ... MAIN
9. Rectifiers ... ON (DC electrical panel??)
10. Stop AI-9V button ... Press to turn off APU
11. Course System ... ON (left wall)
12. Gyros switch ... ON (left wall, row of switches??)
  1. Gyros should respond to cyclic movement.
13. 1-2 mins after turning on gyros, press and hold CAGE buttons for each gyro for a few seconds.
  1. Gyro 1 Failure and Gyro 2 Failure lights should go out, artificial horizon should start working
14. SPUU mechanical stop switch ... ON
15. SPUU OFF button ... Press and check control indicator is left of neutral??
16. Pitch, Roll, and Yaw autopilot channels ... ON
17. SPU-8 Intercom, R-863, JADRO, R-828 ... ON (left wall)
18. Radio altimeter, Autopilot System, Blinker, SPO-10 RWR, CPO ... ON
19. 3 minutes after switching on Course System, it will need to be calibrated:
  1. Operating Mode Switch ... MAG
  2. Synchronize button ... Press and hold for a few seconds
20. ARK-15 mode switch ... COMPASS
21. ARK-U2 switch ... ON (under left elbow)
22. Air Conditioning switch ... CONDITION (under right elbow)

Proceed with remaining takeoff checklist on next page.