301 - Flight - Preflight, Performance Limits

PILOT Before takeoff (hot start or auto cold started) -- WIP
1. RWR ... ON (left wall)
2. Fan ... ON (left wall)
3. IFF ... ON (left wall)
4. DO NOT turn on Airspeed to DISS switch (left wall), that is for emergency use or in case of damage to main doppler system. It will make the moving map and airspeed indicator inaccurate.
5. Lights ... As desired
  - Rotor and formation lights on left wall middle and forward
  - Nav, taxi, and landing lights on left angled panel top
  - Cockpit lighting and dome light on left wall rear
  - Panel lighting knobs on right angled panel bottom and right console rear inboard
  - Autopilot panel lighting on left angled panel above autopilot controls.
1. Radios ... As desired, see steps on other page
2. Turn on sight and pilot weapon switches:
  1. Sight mode SYNC/ASYNC switch ... As desired (UNSYNC recommended) (left side of gunsight base)
    1. UNSYNC is for stationary targets: computer aim point accounts for wind and sideslip.
    2. SYNC is for moving targets: track target for 2-3 seconds and computer provides lead calculation.
  2. Sight mode MANUAL/AUTO switch ... AUTO (up) (left side of gunsight base)
    1. AUTO mode calculates range based on radar altitude and pitch angle. If target is on higher ground than you're flying over, aim below target.
    2. When in MANUAL mode, set range to target with knob in center console.
  3. "RANGE INSERT" Sight distance MANUAL/AUTO switch ... AUT (up) (center console, top row left)
  4. Sight power ON/OFF switch ... SIGHT (up) (center console, top row right)
  5. "FIRE CTRL" Weapon control ON/OFF switch ... ON (up) (center console, center left)
  6. Gunsight brightness ... As desired (GRID BRT knob on right side of gunsight base)
  7. Gunsight glass position ... As desired (Shift-Coll. Metal Switch 1 forward/back to unlock/unlock, Coll. Metal Switch 1 forward/back to adjust)
  8. Aux Stores Light switch ... ON (turns on pylon lights at bottom of center console) (front right panel, bottom)
3. Arm weapons ... Front seat (LCtrl-W or Trim Hat Press, Trim Hat up long to tell Petrovich to do it, takes 5-7 minutes)
4. Doppler navigation system ... As desired (right angled panel), also set heading bugs if desired.
5. Engine dust protection systems ... As needed (green guarded switch on left wall front, below fire extinguisher buttons, left of R-863 radio controls)
6. Engine de-icing systems ... As needed (right console rear outboard) (to enable, turn on all switches on ANTI-ICING SYSTEM panel except leave MAN/AUTO on AUTO??)

GUNNER Before takeoff, for human gunner only -- WIP
1. Main Weapon Safety switch ... ON (or press B2 button when in back seat)
2. USR-24 power switch ... ON
3. USR-24 test switch ... OPER
4. Pitot heat ... ON if OAT <= 5 deg C (front seat??)

Performance limits
- Max fully loaded speed: ~310 kph (167 kts) (with 4x ATGM + 4x rocket pods or 8x ATGM + 2x rocket pods)
- Vne speed: 335 kph officially. Retreating blade stall happens ~370 kph, may roll uncontrollably to the right; flatten collective immediately to attempt recovery.
- Best climb speed: 130-140 kph
- Engine power limits:
  - Max Rated/Takeoff: 990 deg C TIT, 101% N1, 6 minutes
  - Max Limited Cruise: 955 deg C TIT, 99% N1, 60 minutes
  - No time limits below these, but higher temps and RPM may reduce engine service life.
- Main rotor RPM limits:
  - Max Rated/Takeoff: 103% RPM max, 20 sec; 88% RPM min, 30 sec
  - Max Limited Cruise: 101% RPM, 20 sec
  - Below Max Limited Cruise: 103% RPM, 20 sec
- Normal cruise rotor RPM: 93-97%
- Generator cutoff RPM: 86-88%