302 - Flight - Radios, Countermeasures, Jettison, Navigation

Radio setup and tuning
COM1	R-863	VHF/UHF	100.000 to 399.975 MHz??*	AM/FM	Primary radio
COM2	Yadro-1	HF	2 to 17.999 MHz	AM/SSB
COM3	R-828 (Eucalypt-M24)	LVHF	20.000 to 59.975 MHz	FM

* Conflicting info in GR video vs Chuck's Guide. Chuck's says min freq is 200.000, GR says 100.000, radio definitely works on freqs below 200.
All
1. On ICS panel (left wall):
  1. Set RADIO/ICS switch to RADIO.
  2. Set Radio Source Selector Knob to desired radio.
    - SRS doesn't work with this as expected. You must use the SRS Radio 1/2/3 buttons to transmit on the desired radios, which works regardless of what the Selector Knob is turned to. Possible bug in SRS.
R-863 radio -- AM/FM, 220 MHz to 399.975 MHz
1. On R-863 control panel (left wall forward, below fire extinguisher buttons):
  1. Use red cross-shaped knob to set radio channel.
  - Verify the correct frequency in the SRS radio window.
  1. AM/FM switch ... As needed
  2. EM switch ... As needed (monitors guard when on, 121.500 or 243.000??)
  3. ADF switch ... OFF, unless using this radio for direction finding with ARK-U2
R-828 radio -- FM, 20.000 MHz to 59.975 MHz
1. On the R-828 control panel (left wall rear):
  1. Turn red cross-shaped knob to desired channel.
  2. Press and hold the small "AUT" radio tuner button until the light turns on. If you let go too soon, it may not be tuned to the right frequency; in that case, turn the knob to a different freq, fully tune with the button, then change back to desired freq and re-tune.
2. ADF-VHF Source switch ... COMM (left wall, just below R-828 control panel) unless using radio for direction finding

Countermeasures setup from back seat
1. Press Trim Hat press to open Petrovich AI menu.
2. Press Trim Hat left to toggle the Countermeasures menu.
3. Change countermeasures as desired:
  1. Interval: Trim Hat up short
  2. Series: Trim Hat right short
  3. Side: Trim Hat down short
  4. Type: Trim Hat down long

Jettison
Flip the red guarded switches in the center console.

Navigate to a beacon (NDB) with ARK-15M
1. On ICS panel (left wall):
  1. Set RADIO/ICS switch to RADIO.
  2. Set Radio Source Selector Knob to ARK-15M.
2. On ARK-15M control panel (left wall)
  1. ARK-15M receiver mode switch ... VOICE
  2. ARK-15M mode knob ... COMP (compass)
  3. ARK-15M volume knob ... As desired
  4. Set channel 1 (left) or 2 (right) ARK-15M frequency to NDB frequency using dial controls on the outside ring, center, and bottom.
  5. Set channel switch to 1 or 2 as needed.
3. On the HSI compass, needle 1 should point to the NDB.
4. You can easily switch back and forth between two NDBs (e.g. inner and outer markers) using the ARK-15M channel selector switch.
5. Set the Radio Source Selector knob back to R-863 for your primary radio.