501 - A/G - Pilot - Petrovich AI

When in back seat:
Petrovich has two modes, "quick" and "full" for lack of official terms.
Quick mode
- Quick mode is to press Gray Reset Hat forward (mapped to Select target with ASP-17/Order to fire).
- If Petrovich has not been assigned a target, the first press orders him to scan the area inside the gunsight for a target. The second press orders him to fire ATGM at target.
Full mode
Full mode is to press Trim Hat press, which brings up the Petrovich reticle. It starts in Target Designation mode. Boxes around numbers are red when weapons are not ready, yellow when weapons are warming up, and light or dark green when weapons are ready.
Target Designation mode:
Left Short	Show countermeasures panel. Change countermeasures as desired: / Interval: Trim Hat up short / Series: Trim Hat right short / Side: Trim Hat down short / Type: Trim Hat down long
Right Short	Change ATGM type
Left Long/Right Long	--
Up Long	If weapons not enabled, commands Petrovich to set all switches for weapon employment. ATGM system takes 3-4 minutes to warm up. / If weapons are enabled, toggles Petrovich's ROE between Weapons Hold (light green) and Weapons Free (dark green).
Up Short	Enable sight gyros (takes 5-7 secs) and scan for targets in direction you're looking (+/-60 deg from centerline). Targets found will be displayed in the Target List (below).
Down Short	Undesignate target, turn off gyros.

Target List mode:
Left Short	--
Right Short	Designates selected target.
Left Long/Right Long	--
Up Short/Down Short	Moves target selector up/down.
Up Long/Down Long	--

If you don't want to engage any of the targets, select any one of them with Right Short to return to Target Designation mode, then command a new search with Up Short.