504 - A/G - ATGMs

9K144 Shturm (AT-6 Spiral) -- Max range ~5.5 km/2.7 nmi/3.1 mi
9M120 Ataka (AT-9 Spiral-2) -- Max range ~6.0 km/3.2 nmi/3.7 mi)
- 9M120 -- Tandem HEAT warhead
- 9M120F -- HE warhead
- 9M120O -- A/A expanding rod warhead and proximity fuze (4 meters)

Petrovich attack with 9K114 Shturm or 9M120 Ataka ATGM
All steps done from back seat
Select Weapon knob ... MSL/OFF (slaves floating reticle to ATGM sight) (center console)
Hasty attack on target directly ahead:
Press Gray Reset Hat forward to tell Petrovich to scan for a target within the gunsight glass area.
  - 5-7 seconds to activate sight gyros, then floating reticle should move around as Petrovich searches.
If multiple targets found, menu will appear in lower left. Use Trim Hat up/down to select a target, Trim Hat right to select.
  - To do a new search, select any target with Trim Hat right, then press Gray Reset Hat forward again.
Search for targets in a specif‌ic direction:
Press Trim Hat press to bring up Petrovich reticle (boxes around numbers will be green if weapons are ready), look where you want Petrovich to search and press Trim Hat up short.
  - 5-7 seconds to activate sight gyros, then floating reticle should move around as Petrovich searches.
If multiple targets found, menu will appear in lower left. Use Trim Hat up/down to select a target, Trim Hat right to select.
  - To do a new search, select any target with Trim Hat right, then press Trim Hat up short again.
Once a target is designated, get in parameters and f‌ire:
1. When floating reticle has locked on target, fly to put it inside the center ring of the fixed reticle.
2. Petrovich will report when in range. Press Trigger to authorize launch.
  1. Once weapons are activated, Trim Hat up long toggles Petrovich ROE between Weapons Hold (authorize firing with trigger) and Weapons Free (Petrovich fires automatically as soon as within launch parameters)
3. Before taking evasive action, it's a good idea to press Trim Hat down to tell Petrovich to deactivate the Shturm sight to protect the gyros (although he should do it automatically when your bank is > 20 deg).

Manual attack with 9K114 Shturm (AT-6 Spiral) ATGM -- WIP...
1. Select Weapon knob ... OFF/MSL (slaves floating reticle to ATGM scope LOS)
2. MISSILE POWER switch ... ON (front seat)
3. ATGM sight power and guidance unit panel ... ON??
  - Takes 3-4 minutes to warm up, READNS and READY lights will go on when ready.
OBSERV switch ... ON (turns on sight stabilization gyros and opens sight doors)
  - L3 light will start blinking, L4 light will go in in 10-15 seconds, sight is now ready and can be moved.
Missile station select knob ... As needed to select pylon
  - From pilot's perspective, ATGM tubes are numbered: 1, 2, 5, 6, 7, 8, 3, 4
  - MSL ON LNCHR light will illuminate if selected tube is loaded
1. Look through sight and acquire target.
  1. Middle Finger Hat left/right to zoom.
  2. Trim Hat up to tell Petrovich pilot to fly at target.
2. Pilot maneuvers helicopter to put floating reticle inside the inner ring of the fixed reticle.
  1. Red light and continuous tone will sound indicating within launch parameters.
3. Fire missile with...?? Launches after 0.9 sec delay.
4. Radiation Reset button ... Press to reset guidance command radio for next missile
5. IMPORTANT: Turn off OBSERV switch before maneuvering more than 25 deg pitch or bank to prevent gyro malfunction.