201 - Ground - Cold Start

Cold Start -- Using internal batteries
1. Collective ... Full down
2. (default) Throttle twist grip ... MIN (full left on virtual collective) (past physical collective's idle cutoff to minimum)
3. Rotor Brake lever ... Down (off) (handle on floor to right of pilot seat)
4. Battery 1 and 2 switches ... ON (DC POWER panel above right of copilot's head)
5. DC selector knob ... BATT BUSES (DC POWER panel above right of copilot's head)
6. 115 VAC (inverter) switch... AUTO (down) (AC POWER panel above behind right of copilot's head)
  - Don't turn on the 36 VAC switch yet, that's done after startup to save battery power.
Circuit Breaker banks 4-9 ... ON (upper right roof panel, use gang bars under each bank)
Lower center roof panel, except as noted
1. FIRE EXTING switch ... FIRE EXTING (up)
2. SHUT-OFF VALVES LEFT and RIGHT switches ... ON and close guards (red guarded switches)
3. TANK PUMPS switch: SERVICE, LEFT, RIGHT ... ON
4. Start APU:
  1. APU START switch ... START
  2. APU START button ... Press for 2-3 seconds, green AUTO IGNITION ON light should appear.
    1. APU takes 20 seconds to 1 minute to start, should stabilize below 720 deg C, 1.2-2.0 kg/cm^2.
  3. (optional) Use STBY GEN switch to keep batteries charged, but don't use the STBY GEN and start an engine at the same time with the APU.
5. Start engines (should be downwind engine first, but order doesn't seem to matter in the game):
  1. Engine start mode switch ... START
  2. Engine selector switch ... LEFT or RIGHT
  3. Engine START button ... Press for 2-3 seconds, green AUTO IGNITION ON and STARTER ON lights should appear
  4. When left or right engine N1 needle moves (pilot or copilot instrument panel), push left or right Fuel Shutoff Lever forward (red levers on roof above pilot's head)
  5. Wait for engine RPM to stabilize, around 72%.
  6. Repeat for other engine.
6. Engine selector switch ... NEUTRAL (middle position)
7. Throttle twist grip ... MAX (full right on virtual collective)
8. Rotor speed should increase to 95%
Various locations as noted
1. GENERATORS 1 and 2 switches ... ON (AC POWER panel above behind right of copilot's head)
2. RECTIFIERS 1, 2, and 3 switches ... ON (DC POWER panel above right of copilot's head)
3. 36 VAC (inverter) switch... AUTO (down) (AC POWER panel above behind right of copilot's head)
4. APU OFF button ... Press to turn off APU (lower center roof panel)
  - Also turn off the STBY GEN if you turned it on earlier.
Pilot's triangular panel (above left)
1. LEFT ATT IND switch ... ON
2. GYRO CUT OUT switch ... ON
3. AUDIO WARN switch ... ON
4. PITCH LIM SYS switch ... ON (Tail Rotor Pitch Limiting system)
Copilot's triangular panel (above right)
1. DOPP (Doppler system power) switch ... ON
2. COMM RADIO (JADRO 1A) switch ... ON
3. COMP SYS (Gyrocompass system) switch ... ON
4. RIGHT ATT IND switch ... ON
Various locations as noted
1. GMC Mode Switch ... GC (use GyroCompass as main direction source) (lower right roof panel, bottom right corner)
2. FLASH switch ... ON (above right of copilot's head, right of light switches)
3. Pitch and Roll autopilot channels button ... ON (Trim Hat up) (center console, AUTOPILOT panel)
4. Radar Altimeter power switch ... ON (pilot's instrument panel) and set bug as desired, takes about 30 seconds to turn on

Proceed with remaining takeoff checklist on next page.