301 - Flight - Anti-ice System, Countermeasures, Vuichard

Anti-Ice system
- When all switches on anti-ice panel are off, system is in automatic mode.
  - To force on manually, turn on all switches except right-most one.
- If icing is detected, right engine de-icing will begin automatically, and right-hand column of green lights under the panel will illuminate.
- When right engine is stable, you must manually enable de-icing for left engine by switching the left engine switch from AUTO to MAN (up).
- Due to bleed-air use, anti-icing reduces engine power by about 9% when active. Dust protection and IR filters also reduce power but only by about 2-3% each.

UV-26 Countermeasures system
1. Left switch sets dispenser sides (left/both/right). Lights on display indicate selected side(s).
2. Right switch toggles between showing number of flares remaining, and flare program.
3. In flare program mode, display shows current program:
  - 1st number: Number of dispensing pulses
  - 2nd number: Number of flares per pulse
  - 3rd number: Number of seconds between pulses
1. Press NUM (upper left), SEQ (middle left), and INT (upper right) buttons to increment 1st, 2nd, and 3rd numbers respectively (number in parens on button indicates actual number dispensed, e.g. 5=12 flares dispensed, 7=0.25 seconds between pulses)
2. Press RESET PROG button (middle right) to reset to default values (110).

Vuichard Recovery Technique for clockwise rotor
1. Full right pedal (power pedal).
2. Left cyclic for 15-20 deg bank.
3. Raise collective slowly.