302 - Flight - Radios, Navigation

Radio setup and tuning
COM1	R-863	VHF / UHF	100.000 to 149.975 MHz / 220.000 to 399.975 MHz	AM/FM	Primary radio
COM2	YaDRO-1A	HF	2.000 to 17.999 MHz	AM/SSB	Long range radio
COM3	R-828 (Eucalypt-M24)	LVHF	20.000 to 59.975 MHz	FM

All
1. On ICS panel (front and above both pilot and copilot):
  1. Set RADIO/ICS switch to RADIO.
  2. Set Radio Source Selector Switch knob to desired radio.
R-863 radio -- AM/FM, 220 MHz to 399.975 MHz
On center console, set R-863 Unit Switch to Dial to use red cross-shaped knob above pilot, or Memory (default) to set frequency manually by using the center console dials.
1. Set frequency using selected method.
2. Verify the correct channel in the SRS radio window.
R-828 radio -- FM, 20 MHz to 59.975 MHz
1. Go to copilot seat.
2. On the R-828 control panel by right leg:
  1. Turn on R-828 radio.
  2. Set COMPASS/COMM switch to COMM.
  3. Turn red cross-shaped knob to desired channel.
  4. Press and hold small white radio tuner button next to volume control until green SQUELCH light goes off. If you let go too soon, it may not be tuned to the right freq; in that case, turn the knob to a different freq, fully tune with the button, then change back to desired freq and re-tune.

Navigate to a beacon (NDB) with ARC-9
1. Go to copilot seat.
2. On ICS panel (front and above either pilot or copilot):
  1. Set RADIO/ICS switch to RADIO.
  2. Set Radio Source Selector Switch knob to ARC-9.
3. HSI selector switch ... MW (below pilot's HSI compass)
4. On ARK-9 control panel (front ceiling below and left of ICS panel):
  1. Set ARK-9 mode to COMP (compass)
  2. Set the source switch below the ARK-9 panel to primary or secondary as needed.
  3. Set primary or secondary ARK-9 frequency to NDB frequency using dial control on the bottom and on the center. Fine tune using the knob to the left until you hear the morse code of the NDB beacon.
5. The beacon direction arrow on the HSI should point to the beacon.
6. Set the radio audio back to R-863 for your primary radio.

Navigate to an ELT (Emergency Locator Transmitter) with ARK-UD
1. Go to copilot seat.
2. (optional) To hear the beacon signal, on ICS panel (front and above either pilot or copilot):
  1. Set RADIO/ICS switch to RADIO.
  2. Set Radio Source Selector Switch knob to ARC-UD.
3. On ARK-UD control panel (front ceiling below ICS panel), set desired band and channel. MW/DW switch sets band. MW is VHF, DW is UHF.
  1. On MW (VHF) band, channel knob sets frequency:
    1. Channel 1 = 114.166
    2. Channel 2 = 114.333
    3. Channel 3 = 114.583
    4. Channel 4 = 121.500 (VHF Guard)
    5. Channel 5 = 123.100
    6. Channel 6 = 124.100
  2. On DW (UHF) band, all channel knob positions set 243.000 (UHF Guard).
4. Pilot's HSI selector switch ... VHF (below pilot's HSI compass)
5. Set Mode knob to NARROW; you should hear the ELT beacon and the pilot HSI's beacon direction arrow should point to the beacon. NOTE: Only the pilot's HSI pointer points to the beacon.
6. When you get closer and the WIDE light illuminates, set Mode knob to WIDE.
  - (PULSE and RC modes not implemented in DCS.)
Using R-828 radio for arbitrary homing frequency:
1. Tune R-828 radio to frequency. NOTE: Must be specifically set up in Mission Editor to have correct modulation for ARK-UD homing.
2. Set R-828 COMPASS/COMM switch to COMPASS. Pilot's HSI compass should point to beacon??