201 - Ground - Cold Start

Cold Start -- WIP, needs verification
1. Battery/Accumulator switch ... OFF
2. Generator switch ... ON
3. Ground crew ... Ground electric power ON (backslash, F8, F2, F1)
4. Right Circuit Breaker panel switches ... All ON except Battery/Accumulator
5. Fuel Boost Pump switch ... ON
6. Ignition switch ... ON
7. Fuel Transfer Pump switch ... ON
8. Instruments/Lights switch ... ON
9. Throttle ... Idle (fully aft)
10. Starter Button Safety Cover ... Open (guarded switch on outboard throttle handle)
11. Starter button ... Press for 1-2 seconds
12. When engine is at 600 RPM: Fuel Shutoff Valve ... Half (under flaps lever)
13. When engine is at 900-1200 RPM: Fuel Shutoff Valve ... Full open (fully down) (under flaps lever)
14. Engine should stabilize at 2400-2600 RPM, temp <= 650° C.
15. Hydro-Booster lever ... ON (forward) (inboard of throttle handle)
16. Increase speed to 5000 RPM and make sure GENERATOR OFF light goes out at 4500 RPM or higher.
17. Ground crew ... Ground electric power OFF (backslash, F8, F2, F2)
18. Battery/Accumulator switch ... ON
19. Canopy ... Close
20. Cockpit pressurization ... As needed (set dial to Blue, Yellow, or Red, not sure which?? I think yellow is default) (right wall)
21. Oxygen valve ... ON (full counter-clockwise) (left elbow, below air diluter knob)

Follow remaining steps in preflight checklist on following page.