202 - Ground - Preflight, Performance Limits

Preflight checklist
1. Guns ... Arm (three buttons on left side of instrument panel, press and hold until lights on center console come on)
2. Gun safety ... Off (red lever on top of stick) (Flip Down Trigger press)
3. If using external tanks: Drop Tank Signal Switch ... ON (center console)
4. Begin taxi; Rooksie brakes.

Performance limits
- Max speed with external tanks:
  - Small tanks (2x 300 L): 0.9 Mach, 5 Gs
  - Large tanks (2x 600 L): 0.85 Mach
- Service ceiling: 15000 m without drop tanks, 13400 m with drop tanks
- Stall speed:
  - Idle power, flaps and gear extended: 190 kph
  - Idle power, flaps and gear retracted: 200 - 220 kph below 10000 m, 230 - 240 kph above 10000 m
  - Max power, flaps and gear retracted: 200 kph