201 - Ground - Preflight, Performance Limits

General MiG-19 weirdness
- Artificial horizon is backwards, this is not a bug. The Artificial Horizon globe stays in one orientation relative to the outside world, and your plane, with its fixed indicator on the gauge, moves around the Artificial Horizon globe as you maneuver.
- Engines:
  - Throttles fully forward is Nominal/max continuous power.
  - Military Power and Afterburner are engaged with separate buttons once the throttle is fully forward.
  - Pinky Switch up is Afterburner, Pinky Switch down is Mil Power.
  - Buttons must be pressed for 2 seconds, until appropriate lights on instrument panel are lit:
    - Mil lights are round lights above RPM gauge
    - AB lights are red "AB" lights on warning panel to right of RPM gauge
  - You can go from Mil directly to AB, but not the other way around.
  - To get out of Mil or AB mode, pull back the throttle past the "16 deg detent" (about halfway), then you can advance to full Nominal power again.

Before takeoff (hot start or manually cold started)
1. SPO-2B Sirena tail warning RWR ... As needed (only if equipped in mission editor) (small control box on left forward canopy rail, just above signal flare buttons)
2. Radio ... As needed:
  - There are 6 pre-defined radio channels only (set in the Mission Editor). Press the channel buttons to select. Radio control panel is on left console in front of throttle.
Lights ... As desired:
  - Navigation and landing/taxi lights ... top left instrument panel, hidden up in the top corner
  - Cockpit instrument fluorescent lighting ... dials on right wall upper middle
  - White flood light ... round knob on top of floodlight mounted under right wall upper middle
    - There is no similar white light for the left side.
1. Nosewheel brake lever ... Off (horizontal) (upper left instrument panel, near bottom left corner of gunsight base)
2. Begin taxi, Rooskie brakes, use brake lever with rudders for differential braking.

Performance limits
- Afterburner time: <6000 m, 6 min; >6000 m, 10 min
- Military Power time: <6000 m, 6 min; >6000 m, 10 min
- Engine Altitude limits:
  - 14 km - 16 km, throttles should be moved slowly, at least 5 sec from Idle to Nominal.
  - Over 16 km, only use Mil or AB.
- G limits:
  - Positive: 8 G clean or with rocket pods, 5 G for external tanks or bombs, 6 G for A/A missiles
  - Negative: max 10 seconds if in Mil or AB, 15 seconds otherwise
- Fastest climb speed: Mach 0.88-0.9
- Max speeds:
  - Landing gear extended: 500 kph
  - Flaps 15 deg (takeoff position): 800 kph
  - Flaps 25 deg (landing position): 400 kph??
  - VNE airspeed: 1370 kph (IAS??)
  - Droptanks: 1000 kph (will be jettisoned automatically if you go faster)
    - When jettisoning tanks, recommended speed is 400-800 kph.
  - Drag chute deployment: 300 kph
  - Wheel brakes: 210 kph (faster may overheat them and damage tires)
  - Tire speed: 340 kph