501 - A/G - Guns, Bombs, Rockets

Fence In
1. Right wall switches: Bottom row, all on except rear 2. Top row, all on except front 2 and rear 1.
2. Left wall switches: All on except rear 4.
3. Left and Right Gun Arm buttons ... Press and hold for at least 2 seconds each (B4 and B5 buttons, or left front canopy rail) until red arming lights (center console between legs) are lit
4. ARM BOMBS FUSE switch ... ON (center console between legs, top left corner)

Guns -- 2x NR-30 30mm cannons, 73 rounds each
1. ASP-5 Sight Aiming Mode knob ... NR-30 (left side wall) (Gray Reset Hat backward)
2. ASP-5 Sight Operational Mode switch ... OPTICAL (up) (left side wall) (Middle Finger Hat press to toggle)
3. ASP-5 Sight Cage/Uncage lever ... CAGE (left side of gunsight base) (Rear Thumb Button press to toggle)
4. Gunsight depression ... 0.0 mil (black knob on right side of gunsight base)
5. Put pipper on target and fire with trigger. Adjust as needed.

Rockets -- S-5M 55mm (2.2 inch), 8 rockets per pod, max of 4 rocket pods
1. ASP-5 Sight Aiming Mode knob ... ROCKET PODS (left side wall) (Gray Reset Hat right)
2. ASP-5 Sight Operational Mode switch ... OPTICAL (up) (left side wall) (Middle Finger Hat press to toggle)
3. ASP-5 Sight Cage/Uncage lever ... CAGE (left side of gunsight base) (Rear Thumb Button press to toggle)
4. Gunsight depression ... -1.2 mil recommended for close range (black knob on right side of gunsight base)
5. Rocket Salvo Mode switch ... As desired (left side wall):
  - 1 RO -- 1 rocket per pod per trigger press
  - AUTO -- Salvo all rockets with single trigger press, 0.5 seconds interval
  - 4 RO -- 4 rockets per pod per trigger press, 0.5 seconds interval
Press trigger to fire.
  - Remaining rockets per pod are shown with row of lights on left wall above ASP-5 Sight Aiming Mode knob.

Bombs -- FAB-50, FAB-100M, FAB-250 GP bombs, max of 2 bombs
1. ASP-5 Sight Aiming Mode knob ... BOMBS (left side wall) (Gray Reset Hat left)
2. ASP-5 Sight Operational Mode switch ... OPTICAL (up) (left side wall) (Middle Finger Hat press to toggle)
3. ASP-5 Sight Cage/Uncage lever ... CAGE (left side of gunsight base) (Rear Thumb Button press to toggle)
4. Gunsight depression ... ?? mil (black knob on right side of gunsight base)
5. Bomb Release Mode switch ... As desired (left side wall):
  - MANUAL -- Drops 1 bomb per trigger press (does not fly well with asymmetric load)
  - AUTO -- Drops both bombs simultaneously
Press trigger to drop.