302 - Flight - Fuel Management, Jettison, Engine Restart, Autopilot

Fuel Management
- Full internal fuel = 2750 L
- If centerline tank is equipped, center console will have CENTER FUEL TANK light (regardless of whether the tank is full or empty).
- If wing tanks are equipped, center console will have UB POD EMPTY 3 and UB POD EMPTY 4 not lit, and PYLON 3 OUTER and PYLON 4 OUTER lit.
- Caution light messages in the order they will appear (lights may flicker before they come on solid, numbers below are for when they are on solid):
FUEL PODS EMPTY A (center console)	3000 L remaining.
FUEL PODS EMPTY W (right wall forward)	2750 L remaining (100% fuel). Indicates all external tanks are empty.
FUEL TANK NO 1 GROUP (right wall forward)	800 L remaining (~26% fuel).
FUEL 450 L (right wall forward)	450 L remaining (~15% fuel).
FUEL TANK NO 3 GROUP (right wall forward)	300 L remaining (~8% fuel).
DISP TANK EMPTY (right wall forward)	100 L remaining (3% fuel). Fuel starvation imminent when flickering. Engine dies when light is on solid.

Jettison
- Centerline fuel tank jettison with T2 switch (controls "Drop Center Fuel Pod"), default key is RCtrl+PageUp. The cockpit button is on the front of the stick.
- Wing fuel tank jettison is a yellow guarded button on the top row of the instrument panel, left of center.
- IMPORTANT: If you jettison external tanks before they are empty, manually set the fuel gauge to 2750 L, or it will not show the correct amount remaining.

Engine restart
1. Throttle to idle.
2. Dive to maintain 450 kph minimum if under 8000 m, 550 kph minimum if over 8000 m.
3. Engine Emergency Air Start switch ... ON (on wall above throttle handle)
4. Engine should spool up. When 60-70%, throttle back up slowly to relight.
5. Engine Emergency Air Start switch ... OFF
In case of compressor surge (loud banging noise, typically at high Mach numbers 1.8+)
1. Anti-surge shutters switch ... MANUAL (down) (red semi-guarded switch, left wall)
2. Turn off afterburner.
3. Decrease speed (reduce throttle, climb, or use airbrakes).
4. When banging sounds stop, Anti-surge shutters switch ... AUTO (up).
5. Resume normal flight.

Autopilot (SAU aka AFCS) -- WIP
- There are 4 autopilot modes:
  - Automatic -- Used for PMRG (Russian version of ILS) approaches, controls everything but throttle and flaps
  - Directional -- Used for PMRG approaches, shows visual cues only with yellow needles on HSI
  - Stabilization -- Dampers
  - Recovery -- Level autopilot, controls everything but throttle and flaps
- Autopilot control panel in on left wall forward bottom, in front of throttle
- Stick has one button for Recovery mode, and one button for disengage