501 - A/G - Stores List

Pods:
- ASO-2	Chaff/flare launcher (station 6 only)
- SPRD-99	JATO bottles (station 6 only)
- UPK-23-250	23mm gun pod (stations 2/4 only)
- SPS-141-100	ECM jammer (station 3 only)

AG Missiles
Kh-66 GROM	Radar beam-riding A/G missile (stations 2/4 only)

Bombs:
- BL-755
- BetAB-500	Concrete piercing bomb, low-drag (no parachute or rocket)
- BetAB-500ShP	Concrete piercing bomb, high-drag (parachute and rocket)
  - Drop BetAB-500ShP between 150-1000 m
- FAB-100	GP HE bomb
- FAB-100 x 4	MER with 4x GP HE bomb
- FAB-250	GP HE bomb
- FAB-500 M62	GP HE bomb
- RBK-250 - 42 PTAB-2.5M	Cluster bomb, AP
- RBU-500-255 - 30x PTAB 10-5	Cluster bomb, AP
  - Drop RBKs at 300 m minimum
- RN-24	Nuke (banned on many servers)
- RN-28	Nuke (banned on many servers)
- SAB-100	Illumination Bomb, drop between 1000-3000 m, illumination lasts 1-5 minutes

Rockets:
- S-24A	??
- S-24B	240 mm, 123 kg blast/frag warhead, 2 km max range
- S-25 OFM	340 mm, 190 kg blast/frag warhead, 4 km max range
- UB-16UM	16x S-5M rockets, 57 mm, HE warhead, 3-4 km max range
- UB-32M	32x S-5M rockets, 57 mm, HE warhead, 3-4 km max range