301 - Flight - Takeoff, Landing, RWR, Navigation, Autopilot

Takeoff
1. Flaps ... Up.
2. Verify Autopilot Damper ... ON (Autopilot buttons on left console forward vertical panel, top left light should be on) (LAlt-1) (gives Master Caution beeps on takeoff if disabled)
3. Begin takeoff run.
4. Rotate at 270 kph.
5. DO NOT OVERROTATE, very easy to tailstrike.

Landing
1. Under 400 kph, put down gear and flaps.
2. Landing speed ~220 to 240 kph.??
3. Keep vertical speed low, landing gear is weak.
4. Use drag chute if needed (Shift-T5 down). WARNING Don't press the button again until you want to drop the chute.

RWR
- Light in outer ring of large circles indicates primary threat direction.
- Lights in small dots just inside those indicates secondary threats.
- Ring of dashed lines on the inside indicates range/signal strength of primary threat, weakest is all the way to the right, and getting stronger to the left. Ownship marker is the triangle at the left.
- Lights in bottom row of dashes and letters is primary (dashes) and secondary (letters) threat:
  - П	З	X	H	F	C
  - AI radar	LR radar	MR radar	SR radar	EW radar	AWACS
- B and H lights in the center of the plane show relative elevation of primary threat. If both are lit, threat is co-altitude.
- Red flashing circle in the center around the plane is radar lock warning.
- Press Shift-E1 press to toggle RWR to filter out acquisition radars.

Navigation
- Press B5 to cycle NAV Master Modes: No Task, En Route, Return, and Landing.
- Nav mode is indicated in bottom left of HUD, and distance is shown in bottom center. Modes:
  - No Task -- Nothing in the HUD.
  - En Route -- "ENR" in HUD. Navigates to regular pre-planned waypoints.
  - Return -- "RTN" in HUD. Navigates to the runway approach point for the selected airport ID (see list on next page).
  - Landing -- "LNDG" in HUD. Navigates to the end of the actual runway for the selected airport ID (see list on next page).
- HSI indicator also shows navigation information:
  - Distance to the next waypoint in top left corner.
  - Green needle with a diamond is the direct bearing to the waypoint.
  - Double-line white arrow is the course deviation indicator. The CDI shows a bearing to get back onto the line between the previous and current waypoints, and is what the autopilot Route Following mode will follow.

Autopilot -- WIP/TODO
- Press shift-Trim Hat down for level autopilot.
- Press shift-Trim Hat up or shift-Trigger 2nd Stage to disengage AP.
- You can also disengage by moving the stick more than a certain amount, but that may mess up your trim.
- Hold shift-Trigger 1st Stage to temporarily override autopilot. When released, autopilot will be reset to current altitude and heading.