301 - Flight - Takeoff, Landing, Engine relight

Takeoff
1. Check canopy closed and locked, speedbrakes closed (A.F. light on instrument panel upper left should be out).
2. Flaps ... Half (T6 down once, flaps lever just behind and inboard of throttle, indicator on instrument panel top left)
3. Taxi to takeoff position, brakes will hold full mil power.
4. Take off with full afterburner.
5. Rotate around 120 kts to 12 deg, faster if heavier. Takeoff around 150 kts.
6. Gear up before 240 kts.
7. Flaps up before 300 kts (full flaps max 225 kts).
  - LIM light (instrument panel far left) will illuminate and warning beep will sound if approaching gear/flaps speed limit.
1. Best climb speed:
  1. Clean:
    1. Mil: 470 kts IAS, M 0.92
    2. AB: 500 kts IAS, M 0.95
  2. With 2x drop tanks:
    1. Mil: 422 kts IAS, M 0.84
    2. AB: 475 kts IAS, M 0.92
  3. Interception climb schedule:
    1. Climb subsonic as above to 30,000 ft.
    2. Level off and accelerate to 610 kts.
    3. Maintain 610 kts and climb to 36,000 ft.
    4. Level off and accelerate to M 1.8.
    5. Maintain M 1.8 and climb to desired altitude.

Landing
1. Prohibited to use air brakes while landing. Use on approach is OK, but must be retracted before touchdown.
2. Under 250 kts??, gear and flaps full down.
3. HUD mode switch ... V (Approach mode) (right console forward inboard)
  - Master Arm must be OFF in order for Approach Mode to work.
1. On-speed is 11 deg AOA (green indicator on AOA meter left of HUD)
2. Trim to maintain pitch angle.
3. Max landing weights and rate of descent:
  1. Normal: 9,000 kg (19,842 lbs), 550 ft/min
  2. Exceptional: 11,000 kg (24,251 lbs), 395 ft/min
  3. Emergency: >11,000 kg, as slow as possible <300 ft/min
4. First short broken line below horizon line on HUD is 2.5 deg glideslope line. Put velocity vector dot on glideslope line and align both with runway threshold.
5. When over runway threshold, reduce power and flare to 12-13 deg AOA.
6. After touchdown, fully retract flaps.
7. Optional:
  1. Aerobrake by maintaining 12-13 deg AOA until about 120 kts.
  2. Or deploy drogue chute (green handle on left forward canopy rail).
8. Enable high-gain NWS (Flip-down Trigger press, DIR button on center console between legs, top left, is pushed in slightly if enabled)

Engine relight
Placard with process is on the left side wall under canopy rail.
1. Relight only below 20,000 ft. If below 10,000 ft, relight attempt not recommended as you may run out of altitude??
2. Descend, maintaining at least 230 kts, 300 kts preferred. Try to keep engine RPM above 2,600 or alternators will disengage (which also kills the main altimeter; backup altimeter will still work).
3. Throttle ... IDLE, then CUTOFF (Bottom Thumb Button press)
4. Master valve control switch ... OFF (right console rear outboard, on CABIN panel) (not strictly needed)
5. Relight switch ... Forward (on inboard side of throttle base) (shift-Bottom Thumb Button press)
  - Switch will automatically disengage after 30 seconds.
1. Throttle ... Approximately halfway between idle and mil power
2. Within 30 seconds, RPM should begin increasing and temp should increase past 250 deg (TUYERE gauge under RPM gauge)
  - If engine fails to relight, wait 30 seconds for the Relight switch to reset, then cut throttle completely (IDLE then CUTOFF) before attempting again.
1. Increase throttle to desired power.
2. Master valve control switch ... ON (right console rear outboard, on CABIN panel)
3. Reset alternators if needed with CONV/AUTO/REARM switch to REARM (momentary) and then back to AUTO (right console forward vertical panel)