302 - Flight - Navigation, Autopilot

TACAN navigation
TACAN panel is on right console.
1. Tune to TACAN channel with knobs.
2. Set mode with outer ring:
  1. OFF -- Off.
  2. REC -- Receive, provides only bearing information.
  3. T/R -- Transmit/Receive, provides bearing and range.
  4. A/A -- Air to Air, airborne TACAN stations (e.g. tankers).
3. When tuned, you should see a green light on the TACAN panel and hear the Morse identifier. You can set the TACAN volume on the volume controls panel (left console forward), TAC knob. (Not currently working??)
4. On HSI gauge (right lower instrument panel):
  1. Mode lever (bottom):
    1. AR -- Arret (OFF)
    2. VT -- VOR and TACAN only
    3. TE -- Radar cursor bearing only
    4. TT -- VOR/TACAN and radar cursor bearing
  2. Vector mode knob (upper right):
    1. N -- Shows bearing and distance to TACAN beacon itself.
    2. VECT ADD -- Shows bearing and distance to an offset point relative to the TACAN beacon specified by RELEV (magnetic bearing) and DIST (nmi) knobs.
  3. Large arrow on HSI shows TACAN bearing or offset bearing.
5. To set a course, use Omnibearing selector knob (right console next to TACAN panel)
  1. Set knob outer ring to TAC, then turn knob to desired course.
  2. Main artificial horizon indicator shows course deviation with vertical yellow bar. Top left of artificial horizon shows TO or FR indicating whether you're flying to or from the beacon. CDI bar always shows TO, so if flying FR you will need to correct in the opposite direction.

VOR/ILS
VOR panel is on right console.
1. Turn on VOR receiver with left knob outer ring to M (turn off with A).
2. Tune to VOR frequency with knobs.
3. When tuned, you should hear the VOR morse identifier. You can set the VOR volume on the volume controls panel (left console forward), VOR knob. (Not currently working??)
4. On HSI gauge (right lower instrument panel):
  1. Mode lever (bottom):
    1. AR -- Arret (OFF)
    2. VT -- VOR and TACAN only
    3. TE -- Radar cursor bearing only
    4. TT -- VOR/TACAN and radar cursor bearing
  2. VOR only gives bearing, not distance, therefore vector mode cannot be used with VOR, only with TACAN.
  3. Small arrow on inside of compass ring on HSI shows VOR bearing.
5. To set a course, use Omnibearing selector knob (right console next to TACAN panel)
  1. Set knob outer ring to TAC, then turn knob to desired course.
  2. Main artificial horizon indicator shows course deviation with vertical yellow bar. Top left of artificial horizon shows TO or FR indicating whether you're flying to or from the beacon. CDI bar always shows TO, so if flying FR you will need to correct in the opposite direction.

Autopilot system -- WIP needs verification
- Autopilot control panel is on upper left instrument panel.
- Engage autopilot by holding the autopilot disconnect trigger on stick (Trigger stage 1) while pressing the PA button on the autopilot control panel. This engages attitude hold, called "basic functions" mode.
- Press corresponding button to engage autopilot mode:
  - PA -- Attitude hold (default mode, "basic functions" mode)
  - ALT -- Altitude hold (doesn't work between 0.95 and 1.05 Mach due to transonic effects)
  - CAP -- Heading hold
  - R -- Localizer ("Runway")
  - G -- Glideslope
- Press autopilot disconnect trigger on stick (Trigger stage 1) to turn off advanced modes and return to "basic functions" (attitude hold) mode.
- Press autopilot disengage button on stick (Lower Gray Button), or PA button on autopilot panel, to completely turn off autopilot.
- The heading for the Heading Hold mode is selected using the CAP AFFICHE (Heading Selection) knob on the right console. Selected heading is displayed with hollow white "V" on the outside of the HSI compass rose.