203 - Ground - Failure warning light panel

Failure warning light panel:
BATT / battery disconnected or dead	ALT1 / alternator 1 fail	ALT2 / alternator 2 fail	TR1. / transformer-rectifier 1 fail (DC system)	SEC~ / inverter supplying AC system
B.P. / engine fuel feed system, low pressure	BP.G / left fuel pump, low pressure	BP.D / right fuel pump, low pressure	TR.2 / transformer-rectifier 2 fail (DIC system)	NIV / low fuel, feeder tanks < 250 L
HUILE / oil pressure low	E.P. / electric hydraulic pump active > 8 seconds	HYD.S / hydraulic emergency circuit, low pressure	HYDR.1 / hydraulic 1, low pressure	HYDR.2 / hydraulic 2, low pressure
REG.O2 / oxygen regulator fail	5mnO2 / 5 mins of oxygen remaining	T.EQ / equipment bay temperature too high	T.CAB / cockpit temperature too high	P.CAB / cockpit pressure low (alt. equiv. > 30k ft) or canopy unlocked??
TRIM / automatic pitch/roll trim system fail (autopilot and manual trim not affected)	PA / autopilot disengaged or fail	CAP / autopilot heading fail	ANEMO / pitot or static pressure fail or probe heat off	C.AERO / air data computer fail
LACET / both yaw circuits fail, yaw damper not operational	TANG. / both pitch circuits fail, pitch damper not operational	ROUL. / both pitch or yaw circuits fail, roll damper and autopilot not operational	EMP. / one pitch circuit fail	DIR / one yaw circuit fail
T / not a light??	T.O2 / not a light??	HYPER. / combat flaps not at commanded position or activated outside allowed envelope	MODUL / excessive alternator driving torque	VAM.D / bleed valves position not matching commands