201 - Ground - Cold Start

Cold Start Checklist -- No Auto Start currently avialable
NOTE: Strikeout lines indicate items that should be set by default in a cold start.
1. Parking brake ... Set (to re-set: hold brake, press and hold LAlt-T while releasing brake)
2. Check Brake pressure ... 200 psi min (gauge on bottom of instrument panel)
3. Electric Power Master Switch ... ON (upper instrument panel, right side, hidden under dash, above and connected by gang bar to a guard over the 4 magneto switches)
4. Fuel cocks ... Outer tanks (white painted tips to outsides, press B4 and B6) (behind pilot seat at navigator's left elbow)
5. Pressure venting cock ... Open (up, press Shift-B4 or Shift-B6) (behind pilot's seat at navigator's left elbow)
6. Supercharger ... MOD (low, switch down) (on rear side wall of throttle quadrant, obscured by guard)
7. Mixture ... Full rich (lever down, press Throttle Top Hat up)
8. Radiators ... Closed (switches on dashboard right eyebrow panel, press Throttle Bottom Hat up and down to toggle left and right respectively)
9. Fuel pump switch ... Off (right wall top row switches)
10. Crack throttle open, approx 1/2 inch
11. Prop RPM ... Max (move Throttle Flaps lever forward)
12. Open window or door, contact Ground Crew ... Start priming engines
13. Start left engine:
  1. PORT magneto switches ... ON (two switches, upper right instrument panel hidden under dash)
  2. Left STARTER and BOOST COIL covers ... Open (above and right of magneto switches)
  3. Click STARTER button with left mouse button and hold, then click BOOST button with right mouse button and hold.
  4. When engine is started (may take several seconds, wait for 1000 RPM or more), release both buttons and close covers.
  5. Increase left throttle to get to 1200 RPM to begin warming up the engine.
14. Start right engine:
  1. STBD magneto switches ... ON (two switches, upper right instrument panel hidden under dash)
  2. Right STARTER and BOOST COIL covers ... Open (above and right of magneto switches)
  3. Click STARTER button with left mouse button and hold, then click BOOST button with right mouse button and hold.
  4. When engine is started (may take several seconds, wait for 1000 RPM or more), release both buttons and close covers.
  5. Increase right throttle to get to 1200 RPM to begin warming up the engine.
15. When each engine reaches 40 dec C coolant and 15 deg C oil, open the radiator for that engine (switches on dashboard right eyebrow panel, or press Throttle Bottom Hat up and down to toggle left and right respectively).

Proceed with rest of preflight checklist on next page.