202 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start)
1. Gunsight power ... ON (right canopy rim)
2. Radiator flaps ... Open (switches down) (front canopy rim, right side)
3. Pitot heat ... As needed (right canopy rim)
4. Lights ... As desired (TODO)
5. Radios ... As needed (TODO)

Performance limits
- Fuel: 3269 lbs internal
  - with 2x 50 gal drop tanks (361 lbs ea.) = 3991 lbs
  - with 2x 100 gal drop tanks (722 lbs ea.) = 4713 lbs
- Speeds:
  - Bomb bay doors: 351 mph/305 kts
  - Landing gear: 178 mph/155 kts
  - Flaps up to 25 deg: 201 mph/175 kts
  - Flaps full down: 150 mph/130 kts
  - Wing tanks jettison: 201-299 mph/175-260 kts, straight and level
- Engines:
  - Max weak mixture boost: +7
  - Mode	Time	RPM	Boost	Coolant °C	Oil °C
    Operational necessity	5 min	3000	+25	125	105
    Max Take-off	??	3000	+18	??	??
    Intermediate	1 hr	2850	+9	125	90
    Max Continuous	No limit	2650	+7	105*	90
* up to 115 for a short period